## Slide 1
Processor Instruction Set Architecture & Language
Lishan Yang
GMU CS695
Advanced Computer Architecture
Spring 2023
Notes: https://www.cdw.com/product/hp-ddr5-32-gb-dimm-288-pin-4800-mhz-pc5-38400-unbuffered/7017334

## Slide 2
Processor Instruction Set Architecture & Language
Lishan Yang
GMU CS695
Advanced Computer Architecture
Spring 2023
Intel Skylake (CPU)
US Capitol
Notes: https://www.cdw.com/product/hp-ddr5-32-gb-dimm-288-pin-4800-mhz-pc5-38400-unbuffered/7017334

## Slide 3
Processor Instruction Set Architecture & Language
Lishan Yang
GMU CS695 Advanced Computer Architecture
Spring 2023
Lecture 2
Reference:
CMPE 140, Hyeran Jeon
CMPE 140, Donald Hung
CMPE 140, Haonan Wang
Computer Architecture: A Quantitative Approach
Licensed for use under a Creative Commons Attribution-NonCommercial-ShareAlike 3.0 Unported License.

## Slide 4: Instruction Set Architecture & Microarchitecture
Instruction Set Architecture
  the programmer’s view of the computer, defined by a set of instructions that each specifies an operation and its operand(s)
Microarchitecture
  the way that the ISA is implemented in hardware
Application
Compiler/Libraries
Operating system
Circuits
Semiconductor physics
Instruction Set (ISA)
Microarchitecture

## Slide 5: What Does the ISA Deal With Specifically?
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Example: a C program that reads
two integer values from “file.txt” file
and prints the sum of them.
Processor
(CPU)
Understands and executes each line of the code.
Uses fast on-chip memories
Memory
(DRAM)
Provides operands to CPU
(*fp, size, sum, numbers[2])
Storage
(HDD)
Provides file inputs and program code
(file.txt)

## Slide 6: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
Dynamic data: heap
  e.g., malloc in C, new in Java
  Grows from bottom (lower address) to top (higher address)
Stack: temporal storage for functions
  e.g., return address of sub-functions, local variables
  Grows from top to bottom
Address Content

## Slide 7: Memory Layout
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Compiled machine code
numbers[1]
numbers[0]
Compiled machine code

## Slide 8: Memory Layout
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Compiled machine code
Return address
*fp
size
sum
Stack region for myfunction
numbers[1]
numbers[0]

## Slide 9: Memory Layout
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Compiled machine code
Return address
*fp
size
sum
Stack region for myfunction
numbers[1]
numbers[0]

## Slide 10: Memory
(CPU)
Register
Cache
Memory
Disk
Tape
Sizes
100s of Bytes
KB ~ MB
MB ~ GB
GB ~ TB
>TB
Speed
10 ns
100 ns
1 us
1 ms
1 sec

## Slide 11: Memory Access Is Slow
Variables are all stored in Memory, which is outside of CPU
  Slow..
How can we execute the operations faster?
  Use on-chip memory
Compiled machine code
Return address
*fp
size
sum
numbers[1]
numbers[0]

## Slide 12: Register File
Register File
  On-chip memory that stores “Registers”
Registers
  Temporal space to maintain operand values and calculation results before storing back to memory
  Presented with “$” + “register id” in MIPS processor
    i.e. $0 : 0th register,
    $1 : 1st register
Compiled machine code
Return address
*fp
size
sum
$0
$1
$2
…
$31
Register File
numbers[1]
numbers[0]

## Slide 13: Typical Execution Steps
  Load operand values from memory to registers
  Do computation on registers
  Move the results from register to memory
Compiled machine code
Return address
*fp
size
sum
$0
$1
$2
…
$31
Register File
numbers[1]
numbers[0]

## Slide 14: Operations in Hardware
Hardware can do one operation at a time
  Arithmetic operations
    add, sub, mult, div, …
  Data movement
    move, load data, store data, …
  Logical operations
    shift, and, or, xor, …
  Conditional operations
    jump, branch on condition, …
Format of assembly instructions that uses register operands
  Command Result, Operand 1, Operand 2
  E.g. C = A + B  Add C, A, B (A, B, C should be replaced by register id)
ALU (Arithmetic Logic Unit)
By Lambtron - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=36975996

## Slide 15: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Operations involved:
Value of ‘a’ is loaded from mem to $3
Value of ‘b’ is loaded from mem to $2
Add operation done on $2 and $3
Value of ‘c’ is stored to mem

## Slide 16: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
$0
$1
$2
…
$31
Register File
executing line
$3
Stack region
allocation for test()

## Slide 17: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
$0
$1
$2
…
$31
Register File
executing line
$3
a = 1

## Slide 18: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2
…
$31
Register File
executing line
$3

## Slide 19: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2
…
$31
Register File
executing line
$3

## Slide 20: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2
…
$31
Register File
executing line
$3 (1)

## Slide 21: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2 (2)
…
$31
Register File
executing line
$3 (1)
+
$2 (3)

## Slide 22: Code Example: Memory & Registers
C code
MIPS Assembly code
Compile
Compiled machine code
b = 2
a = 1
$0
$1
$2 (2)
…
$31
Register File
executing line
$3 (1)
$2 (3)
c = 3

## Slide 23: Registers of MIPS CPUs
Assembler Name | Register Number | Description
$zero | $0 | Constant 0 value
$at | $1 | Assembler temporary
$v0-$v1 | $2-$3 | Function return values
$a0-$a3 | $4-$7 | Function Arguments
$t0-$t7 | $8-$15 | Temporaries
$s0-$s7 | $16-$23 | Saved Temporaries
$t8-$t9 | $24-$25 | Temporaries
$k0-$k1 | $26-$27 | Reserved for OS kernel
$gp | $28 | Global Pointer (Global and static variables/data)
$sp | $29 | Stack Pointer
$fp | $30 | Frame Pointer
$ra | $31 | Return Address

## Slide 24: HLL vs. Hardware Operations
HLL: High-Level Language
HLL are designed to be understood and programmed easily by programmers
A HLL line may be a combination of multiple assembly instructions
Compile

## Slide 25: A Brief Review
One line of HLL can involve:
  Load operand values from memory to registers
  Do computation on registers
  Move the results from register to memory
  Arithmetic operations
    add, sub, mult, div, …
  Logical operations
    shift, and, or, xor, …
  Conditional operations
    jump, branch on condition, …
  Data load operations
    move, load data, …
  Data store operations
    move, store data, …

## Slide 26: Operations of MIPS CPUs
Note: A, B, C in the table should be replaced by proper register ids
C operator | Assembly Operations | Comments
C = A + B | add C, A, B | Add two values
C = A - B | sub C, A, B | Subtract one from another
C = A * B | mul C, A, B | Multiply two values
C = A & B | and C, A, B | Logical AND operation
C = A ¦ B | or C, A, B | Logical OR operation
C = A ^ B | xor C, A, B | Logical XOR operation
C = A << shamt | sll C, A, shamt | Shift left by shamt
C = A >> shamt | srl C, A, shamt | Shift right by shamt
If (A < B) C = 1 | slt C, A, B | Set if less than
C = Memory | lw C, Memory address | Load value from memory
Memory = C | sw C, Memory address | Store value to memory
If (A == B) go to Addr | beq A, B, address | Jump if A == B
Many more … |  | 

## Slide 27: Exercise: Register Reuse
Example:
- Assume g, h, i and j are loaded to registers, $t0, $t1, $t2, $t3
- HLL:
f = (g + h) – (i + j);
- Assembly (with add & sub operations)?
add $t0, $t0, $t1
add $t2, $t2, $t3
sub $t2, $t0, $t2
Register values are maintained unless overwritten

## Slide 28: About MIPS Assembly
CPUs use their own assembly languages
  Assembly language of ARM, Pentium, Opteron… are all different
MIPS Assembly Features
  Very similar to ARM Assembly
  One of the earliest RISC architectures that used pipelined instruction processing
Developed by MIPS Technologies
  Now maintained by Wave Computing
  Various generations
    MIPS I~V
    MIPS32 (32-bit processor)
    MIPS64 (64-bit processor)
    microMIPS...

## Slide 29: Two types of Computers
  Reduced Instruction Set Computer (RISC): MIPS, ARM, …
    - Operands are in registers
    - Each instruction can do only one operation: Simple but longer codes
  Complex Instruction Set Computer (CISC): Intel, AMD, …
    - Operands can be in registers, stacks, accumulators, in memories
    - Each instruction can do multiple operations: Complex but shorter codes
    - Preferred when memory was very expensive
Check RISC-V
https://riscv.org/

## Slide 30: MIPS Processor Organization
Memory
CPU
$0
...
$31
Integer
Registers
Arithmetic Unit
Multiply
Divide
Lo
Hi
Coprocessor 1 (FPU)
$0
...
$31
Floating
-point
Arithmetic Unit
Coprocessor 0
(Traps and Memory)
VAddr
Cause
Status
EPC
32~64bit
32 bit
Our Focus
Registers

## Slide 31: About MIPS32 Processor
  Instructions are 32-bit wide
  Registers and Computing Logic use 32-bit data
  Memory bus is logically 32-bit wide
  32 general purpose registers (GPRs) for integer and address values
    - A few special ones (i.e. $zero: constant 0, $fp: frame pointer, $sp: stack pointer..)
  32 floating point registers for floating point operations (not our focus)

## Slide 32: MIPS Data Sizes
Integer: 3 Sizes Defined
  Byte (B)
    8-bits
  Halfword (H)
    16-bits = 2 bytes
  Word (W)
    32-bits = 4 bytes
Floating-point: 2 Sizes Defined
  Single (S)
    32-bits = 4 bytes
  Double (D)
    64-bits = 8 bytes
    For a 32-bit data bus, a double needs 2 memory reads

## Slide 33: Byte-oriented vs. Word-oriented Memory
Most processors are byte-oriented
  Can access a word from any byte address
MIPS: Word-oriented
  Words must be aligned to multiples of its size
  Still byte-addressable!
  Provides some simplicity in design
Logical views can be arranged in rows of 4-bytes for word-oriented memories
Proc
Mem
A
D
/
32
/
32
…
12
F3
3B
0x00002
0x00001
0x00000
Logical Byte-Oriented View of Mem
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View

## Slide 34: Endian-ness
Endian-ness refers to the two alternate methods of ordering the bytes in a larger unit (word, long, etc.)
  Big-Endian: IBM, SPARC, Motorola
    Most Significant byte (MSB) is put at the
    starting (low) address
  Little-Endian: Intel, DEC
    Least Significant byte (LSB) is put at the
    starting (low) address
  Supporting both
    MIPS, PowerPC, ARM
The longword value:
Big-Endian
Little-Endian
0 x 1 2 3 4 5 6 7 8
can be stored differently
78
0x00
56
34
0x01
0x02
12
0x03
12
0x00
34
56
0x01
0x02
78
0x03

## Slide 35: Memory Characteristics & Assumptions
Half-word and Word data are addressed with lowest byte address among the bytes in the data
Addresses from left to right follows the same order as addresses from top to bottom
We will use Little-Endian for MIPS in this course
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View

## Slide 36: Memory Organization Example 1
  Example: If the memory layout is given like below
  The byte value in address
  0x0000 is ( )
  0x0001 is ( )
  0x0002 is ( )
  0x0003 is ( )
  0x0006 is ( )
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View
0x3B
0xF3
0x12
0x7C
0x47

## Slide 37: Memory Organization Example 2
  Example: If the memory layout in MIPS is given like below
  The half-word value in address
  0x0000 is ( )
  0x0001 is ( )
  0x0002 is ( )
  The word value in address
  0x0002 is ( )
  0x0004 is ( )
12
F3
3B
7C
47
13
00
8E
…
0x00008
0x00004
0x00000
Logical Word-Oriented View
0xF33B
Incorrect addressing
0x7C12
Incorrect addressing
0x8E471300

## Slide 38: Tips to Remember Endianness
Looks normal (same as writing order) when address is from low to high
Looks strange here
But same as writing order when address is from high to low
word value:
Little-Endian
0 x 1 2 3 4 5 6 7 8
78
0x03
56
34
0x02
0x01
12
0x00
12
0x00
34
56
0x01
0x02
78
0x03
34
56
78
12
…
0x00004
0x00000
Logical Word-Oriented View

## Slide 39: Basic Instruction Formats
Example: Format with 3 registers
  add Rd, Rs, Rt # Rd = Rs + Rt
Command
(operation)
Destination Register
(stores calculation result)
Source Register 1
(stores first operand value)
Source Register 2
(stores second operand value)
Comment

## Slide 40: Basic Instruction Formats
Example: Format with 3 registers
  add $4, $3, $2 # $4 = $3 + $2
$0
$1
$2 (3)
…
$31
Register File
$3 (2)
$4
If $2 and $3 have integer values 3 and 2 each,
$4 will have ( ) after executing this instruction
5
$4 (5)

## Slide 41: R-Type Instructions
We call the instructions that use three registers as R-type Instructions
  2 registers as source, 1 register for result (destination)
Examples:
  sub Rd, Rs, Rt # Rd = Rs – Rt
  mul Rd, Rs, Rt # Rd = Rs * Rt
  and Rd, Rs, Rt # Rd = Rs & Rt
  or Rd, Rs, Rt # Rd = Rs | Rt
  xor Rd, Rs, Rt # Rd = Rs ^ Rt
  slt Rd, Rs, Rt # if (Rs < Rt) Rd = 1; else Rd = 0;
  many more
Replace Rd, Rs, Rt with actual registers

## Slide 42: R-Type Instructions
Exercise:
  Assume that the initial state of register file is like below
  What is $2 value after executing all three instructions?
sub $4, $2, $3
add $3, $3, $4
slt $2, $3, $4
$0
$1
$2 (10)
…
$31
Register File
$3 (8)
$4 (4)
$4 (2)
# 2 = 10 - 8
# 10 = 8 + 2
$3 (10)
# (10 < 2)? No
 $2 = 0
$2 (0)

## Slide 43: Instructions Using Immediate Value
What if you want to use an immediate value?
  E.g. i = i + 1; // add immediate value 1 to i
  addi Rt, Rs, imm # Rt = Rs + imm
Command
(operation)
Destination Register
(stores calculation result)
Source Register
(stores operand value)
Immediate operand
(stores immediate operand value)

## Slide 44: Instructions Using Immediate Value
Example: Instruction format with immediate value
  addi $4, $3, 1 # $4 = $3 + 1
$0
$1
$2 (3)
…
$31
Register File
$3 (2)
$4
If $3 has integer value 2,
$4 will have ( ) after executing this instruction
3
$4 (3)

## Slide 45: I-Type Instructions
We call the instructions that use two registers and one immediate value as I-type Instructions
  1 register and 1 immediate value as source, 1 register for result
Examples:
  subi Rt, Rs, imm # Rt = Rs – imm
  andi Rt, Rs, imm # Rt = Rs & imm
  ori Rt, Rs, imm # Rt = Rs | imm
  xori Rt, Rs, imm # Rt = Rs ^ imm
  beq Rt, Rs, imm # if (Rt == Rs) goto imm; else continue
  lw Rt, imm(Rs) # load a word from (imm + Rs) address to Rt
  slti Rt, Rs, imm # if (Rs < imm) Rt = 1; else Rt = 0;
  many more

## Slide 46: I-Type: Branch Instructions
  Conditional Branches
    Branches only if a particular condition is true
      E.g., Compares Rs, Rt. If EQ/NE, branch to label, else continue
  Example:
if ( a == b ) {
a++;
}
else {
a--;
}
Check condition of if statement
Upon the condition result,
you execute either a++ or a--
TRUE
FALSE

## Slide 47: I-Type: Branch Instructions
  Conditional Branches
    Branches only if a particular condition is true
      E.g., Compares Rs, Rt. If EQ/NE, branch to label, else continue
  Example:
sub $4, $2, $3
add $3, $3, $4
slt $2, $3, $4
Without branch,
instructions are executed
sequentially; line by line
sub $4, $2, $3
beq $3, $4, Label
slt $2, $3, $4
Label: addi $3, $3, 1
Branch instruction checks the condition
and choose either executing next line or
jumping to the specified line
If $3 == $4
If $3 != $4

## Slide 48: I-Type: Branch Instructions
Conditional Branches
  Branch if condition satisfies
  beq Rs, Rt, imm # if (Rs == Rt) goto imm; else continue
  bne Rs, Rt, imm # if (Rs != Rt) goto imm; else continue
Unconditional Branches
  Always branch to label
  b imm # goto imm
  beq $0, $0, imm # goto imm
Pseudo-instruction
Instruction “b imm” is not actually supported by the hardware.
Assembler replaces “b imm” to “beq $0, $0, imm”
Comparing the same
register values
 always equal

## Slide 49: I-Type: Memory Instructions
  Memory operations use special format to present memory address
  Example:
  lw Rt, imm(Rs) # Load a word from address (Rs + imm) to Rt
Command
(operation)
Destination Register
(stores loaded value)
Immediate value
(stores offset value of
the target memory address)
Source operand
(stores base address of
the target memory address)

## Slide 50: I-Type: Memory Instructions
Memory Instruction Example:
  lw $4, 4($3) # $4 = a word data in ($3 + 4)
$0
$1
$2 (3)
…
$31
Register File
$3 (0x7000)
$4
If the initial state of register file and memory
is like illustrated,
a word in ( ) will be loaded to $4 so
$4 will have ( ) after executing this instruction
10
$4 (10)
Memory
10
512
0x0
0x7fffffff
0x7000
0x7004
0x7004

## Slide 51: I-Type: Memory Instructions
Load: move data from memory to register file
  lb Rt, imm(Rs) # Rt = 1-byte data in (Rs + imm)
  lh Rt, imm(Rs) # Rt = 2-byte (half-word) data in (Rs + imm)
  lw Rt, imm(Rs) # Rt = 4-byte (word) data in (Rs + imm)
Store: move data from register file to memory
  sb Rt, imm(Rs) # (Rs + imm) = 1-byte data in Rt
  sh Rt, imm(Rs) # (Rs + imm) = 2-byte (half-word) data in Rt
  sw Rt, imm(Rs) # (Rs + imm) = 4-byte (word) data in Rt

## Slide 52: I-Type: Memory Instructions
Example:
  The initial state of register file and memory are like below
  What is $2 value after executing each of the following instructions?
  lw $2, 0x40($3)
  lb $2, -1($4)
  lh $2, -6($4)
0
Register File
0x7000
0x704C
Memory
0x0
0x7fffffff
0x7040
0x7044
0x7048
0xF8BE97CD
0x134982FE
0x5A12C5B7
$0
$1
$2
$3
$4
$31
…
# $2 = word in 0x7040
# $2 = byte in 0x704B
# $2 = 2 bytes in 0x7046
0x5A12C5B7
0xFFFFFFF8
Note that when executing lb and lh which loads a signed data which is shorter than 4-byte word, the data should be sign-extended to fill 32-bit space of a register.
0x00001349

## Slide 53: I-Type: Memory Instructions
Example:
  The initial state of register file and memory are like below
  How the memory is updated?
  sw $2, 0x40($3)
  sb $2, -5($4)
  sh $2, -2($4)
0x123489AB
Register File
0x7000
0x704C
Memory
0x0
0x7fffffff
0x7040
0x7044
0x7048
0xF8BE97CD
0x134982FE
0x5A12C5B7
$0
$1
$2
$3
$4
$31
…
# 0x7040 = word in $2
# 0x7047 = byte in $2
# 0x704A = 2 bytes in $2
When you store 1- to 2- bytes to memory, other values in the same word should remain unchanged
0x123489AB
0xAB4982FE
0x89AB97CD

## Slide 54: Signed vs. Unsigned Instructions
We use sign extension for lb and lh
  This is because lb and lh are signed instructions
Unsigned instructions
  No need to do sign extension because the values are regarded as positive values always; just fill zeros to the remaining bytes
  lbu $2, -1($4) # load byte unsigned
  # If lb in the earlier example is lbu,
  # $2 will be updated with 0x000000F8
  lhu $2, -6($4) # load half-word unsigned
  # If lh in the earlier example is lhu,
  # $2 will be updated with 0x00001349

## Slide 55: Signed vs. Unsigned Instructions
Other instructions also have unsigned versions
  addu, addiu, subu, divu, multu, …
Example:
  Assume that $2 = 0xFFFFFFFF, $3 = 0x00000001, what is $1 in each instruction?
  slt $1, $2, $3 # signed set less than
  # -1 < +1  $1 = 1
  sltu $1, $2, $3 # unsigned set less than
  # +4,294,967,295 > +1  $1 = 0

## Slide 56: Exercise
Translate the given high-level language code to MIPS assembly.
  Assume that the address of integer variables x, y, and z are in 0x400, 0x404, and 0x408 in the memory, respectively
  $1’s initial value is 0x400
x = y + z;
lw $2, 4($1)
lw $3, 8($1)
add $2, $2, $3
sw $2, 0($1)
MIPS
High-level language
Tasks to do:
Load y value to a register
Load z value to another register
Run add operation
Store the result to memory

## Slide 57: Machine Code of R-Type Instructions
All instructions in MIPS have 32-bit width
  Within 32-bit data, command and three register ids should be presented
  add Rd, Rs, Rt
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits

## Slide 58: Machine Code of R-Type Instructions
Opcode
  Indicate Command/Operation of an instruction with combination of Function field
  Example:
    add
    and
    or
    many more
  R-type instructions always have all zeros in Opcode field and use Function field to distinguish the instructions
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
Rs
Rt
Rd
Shamt
100000
000000
Rs
Rt
Rd
Shamt
100100
000000
Rs
Rt
Rd
Shamt
100101
0
0x20
0
0x24
0x25
0

## Slide 59: Machine Code of R-Type Instructions
Rs, Rt, Rd
  Indicate source and destination register ids used by an instruction
  Example:
    add $5, $4, $3
    and $13, $8, $2
    or $t8, $s0, $s1
  Each field has 5 bits because we have 32 (=25) registers in MIPS
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00100
00011
00101
Shamt
100000
000000
01000
00010
01101
Shamt
100100
000000
10000
10001
11000
Shamt
100101
$4
$3
$5
01000
00010
01101
$8
$2
$13
10000
10001
11000
$s0 (16)
$s1 (17)
$t8 (24)

## Slide 60: Machine Code of R-Type Instructions
Shamt
  Indicate the shift amount that is used for shift instructions only; the other R-type instructions have all zeros in this field
  Example:
    add $5, $4, $3
    and $13, $8, $2
    or $t8, $s0, $s1
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00100
00011
00101
00000
100000
000000
01000
00010
01101
00000
100100
000000
10000
10001
11000
00000
100101

## Slide 61: Shift Instructions
Special format R-type Instruction
  The second operand is an immediate value (shamt) that indicates the amount of shift
Logical Shifting
  Shift towards left/right with filling in 0s
  Example:
    sll Rd, Rt, shamt # Rd = Rt << shamt (Rt: unsigned data)
    srl Rd, Rt, shamt # Rd = Rt >> shamt (Rt: unsigned data)
Arithmetic Shifting
  Shift towards left/right with maintaining the value’s sign bit
  Example:
    sra Rd, Rt, shamt # Rd = Rt >> shamt (Rt: signed data)

## Slide 62: Example: Logical Shift
Shift towards left/right with filling in 0s
Example:
  Assume that the original value of $4 is 0x0000000C
  What is the value of $5 after executing the following shift instructions?
  sll $5, $4, 3 # shift left logical the value of $4 by 3 bits
  srl $5, $4, 2 # shift right logical the value of $4 by 2 bits
0 0 ... 0 0 1 1
Logical Right Shift by 2 bits:
... 0 1 1 0 0 0 0 0
Logical Left Shift by 3 bits:
0’s shifted in…
0’s shifted in…
0 ... 0 1 1 0 0
= +12
= +3
= +96
0x00000003
0x00000060
srl $5, $4, 2
sll $5, $4, 3
$4
0x0000000C
“Shift Right N bits” is used for division by 2N
“Shift Left N bits” is used for multiply by 2N
Careful: Could overflow!
$5
$5
Shift operation should be done in bit level  translate given value to binary first

## Slide 63: Example: Arithmetic Shift
Shift right with replicating MSB
Shift left with filling in 0s
Example:
  Assume that the original value of $4 is 0xFFFFFFFC (= -4)
  What is the value of $5 after executing the following shift instruction?
  sra $5, $4, 2 # shift right arithmetic the value of $4 by 2 bits
1 1 ... 1 1 1 1
Arithmetic Right Shift by 2 bits:
Arithmetic Left Shift by 3 bits:
MSB replicated and shifted in…
0’s shifted in…
1 ... 1 1 1 0 0
= -4
= -1
= -32
0xFFFFFFFF
0xFFFFFFE0
sra $5, $4, 2
sla? $5, $4, 3
$4
0xFFFFFFFC
$5
1.. 1 1 1 0 0 0 0 0
$5
MSB: Most Significant Bit

## Slide 64: Example: Arithmetic Shift
Shift right with replicating MSB
Shift left with filling in 0s
Example:
  Assume that the original value of $4 is 0xFFFFFFFC (= -4)
  What is the value of $5 after executing the following shift instruction?
  sra $5, $4, 2 # shift right arithmetic the value of $4 by 2 bits
1 1 ... 1 1 1 1
Arithmetic Right Shift by 2 bits:
Arithmetic Left Shift by 3 bits:
MSB replicated and shifted in…
0’s shifted in…
1 ... 1 1 1 0 0
= -4
= -1
= -32
0xFFFFFFFF
0xFFFFFFE0
sra $5, $4, 2
sla? $5, $4, 3
$4
0xFFFFFFFC
$5
Notice if we shifted in 0s (like a logical right shift) our result would be a positive number and the division wouldn’t work
Notice there is no difference between an arithmetic and logical left shift. We always shift in 0s.
MIPS uses sll for both logical/arithmetic left shift (no separate sla instruction)
1.. 1 1 1 0 0 0 0 0
$5
MSB: Most Significant Bit

## Slide 65: Machine Code of R-Type Instructions
Shamt
  Indicate the shift amount that is used for shift instructions only; the other R-type instructions have all zeros in this field
  Example:
    sll $5, $4, 3
    srl $5, $4, 2
    sra $5, $4, 2
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00000
00100
00101
00011
000000
000000
00000
00100
00101
00010
000010
000000
00000
00100
00101
00010
000011
3
2
2

## Slide 66: Machine Code of I-Type Instructions
All instructions in MIPS are 32-bit wide
  Within 32-bit data, command, two register ids, and an immediate value should be presented
  addi Rt, Rs, imm
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits

## Slide 67: Machine Code of I-Type Instructions
Opcode
  Indicate Command/Operation of an instruction
  Example:
    addi
    andi
    ori
    many more;
001000
Rs
Rt
Immediate
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
001100
Rs
Rt
Immediate
001101
Rs
Rt
Immediate

## Slide 68: Machine Code of I-Type Instructions
Rs, Rt
  Indicate source and destination register ids used by an instruction
  Example:
    addi $5, $4, 1
    andi $13, $12, 0xA
    ori $t3, $t2, 12
001000
00100
00101
Immediate
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
001100
01100
01101
Immediate
001101
01010
01011
Immediate
$4
$5
$12
$13
$t2 (10)
$t3 (11)

## Slide 69: Machine Code of I-Type Instructions
Immediate
  Indicate the immediate value
  Example:
    addi $5, $4, 1
    andi $13, $12, 0xA
    ori $t3, $t2, 12
001000
00100
00101
0000000000000001
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
001100
01100
01101
0000000000001010
001101
01010
01011
0000000000001100
1
0xA
12

## Slide 70: Machine Code of I-Type Instructions
Special I-Type instructions: Load/Store
  Within 32-bit data, command, two register ids, and an offset value should be presented
  lw Rt, imm(Rs)
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits

## Slide 71: Machine Code of I-Type Instructions
Load/Store in I-Type machine code format
  Example:
    lb $5, 4($4)
    lh $13, 0x10($12)
    lw $t3, -16($t2)
    sb $3, 0xfff0($4)
    sh $2, 8($8)
    sw $s1, 10($s0)
100000
00100
00101
0000000000000100
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
100001
01100
01101
0000000000010000
100011
01010
01011
1111111111110000
4
0x10
-16
101000
00100
00011
1111111111110000
101001
01000
00010
0000000000001000
101011
10000
10001
0000000000001010
0xfff0
8
10
0x20
0x21
0x23
0x28
0x29
0x2B

## Slide 72: Machine Code of I-Type Instructions
Special I-Type instructions: Branch
  uses the same format but needs a special treatment for immediate field value
  beq Rs, Rt, imm
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
Label name to branch

## Slide 73: Branch Target Addressing
PC-relative addressing
  MIPS calculates the branch target address based on the branch instruction’s next instruction’s address
  “Branch to N lines above or below”; not branch to absolute address
  necessary because in many cases, we do not know (at compile time) where our code will be loaded in the memory space
80000 | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …
Assume that the code is loaded
to 0x00080000 in memory
Each instruction is 4-byte long
 Assembly code line address increases by 4 bytes

## Slide 74: Branch Target Addressing
PC-relative addressing
  MIPS calculates the branch target address based on the branch instruction’s next instruction’s address
  “Branch to N lines above or below”; not branch to absolute address
  necessary because in many cases, we do not know (at compile time) where our code will be loaded in the memory space
80000 | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …
Assume that the code is loaded
to 0x00080000 in memory
Each instruction is 4-byte long
 Assembly code line address increases by 4 bytes
Branch two lines below from bne’s next instruction (addi)
 Immediate field will be filled with 2
Branch 6 lines above from b’s next line (Exit)
 Immediate field will be filled with -6

## Slide 75: Branch Target Addressing
Why branch’s next instruction should be considered?
  Because MIPS increments program counter (PC) by 4 before executing an instruction
  This already incremented PC value is used for branch target address calculation
Branch Target Address Calculation
  Target address =
  branch’s next instruction address + offset x 4
  bne $t0, $s5, Exit
    Exit (0x00080018) = addi address (0x00080010) + distance (2) x 4 byte/inst
  b Loop
    Loop (0x00080000) = Exit address (0x00080018) + distance (-6) x 4 byte/inst
80000 | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …

## Slide 76: Machine Code of I-Type Instructions
Branch in I-Type machine code format
  Example:
    bne $t0, $s5, Exit
    beq $0, $0, Loop
000101
01000
10101
0000000000000010
Opcode
Rs
6 bits
5 bits
Rt
5 bits
16 bits
Immediate
32 bits
000100
00000
00000
1111111111111010
2
-6
0x5
0x4
80000s | Loop: sll $t1, $s3, 2
80004 | add $t1, $t1, $s6
80008 | lw $t0, 0($t1)
8000C | bne $t0, $s5, Exit
80010 | addi $s3, $s3, 1
80014 | b Loop
80018 | Exit: …

## Slide 77: Loading an Immediate
What if you want to load an immediate value to a register?
If immediate (constant) is 16 bits or less
  Use ori or addi instruction with $0 register
  Examples : You want to load value 1 to $2
    addi $2, $0, 1 # R[2] = 0 + 1 = 1
    ori $2, $0, 0x1 # R[2] = 0 | 1 = 1
If immediate is more than 16 bits
  Immediates limited to 16 bits so we must load constant with a 2-instruction sequence using the special LUI (Load Upper Immediate) instruction
  To load $2 with 0x12345678
    lui $2, 0x1234
    ori $2, $2, 0x5678
12340000
R[2]
12345678
R[2]
OR 00005678
LUI
ORI
LUI: the immediate value is loaded to the MSB 16 bits of the target register

## Slide 78: Mult & Div Instructions
Memory
CPU
$0
...
$31
Integer
Registers
Arithmetic Unit
Multiply
Divide
Lo
Hi
Coprocessor 1 (FPU)
$0
...
$31
Floating
-point
Arithmetic Unit
Coprocessor 0
(Traps and Memory)
VAddr
Cause
Status
EPC
32~64bit
32 bit
Registers
Lo
Hi

## Slide 79: Mult & Div Instructions
Mult & Div use special registers, lo and hi
Multiplication
  mult Rs, Rt # lo = lower 32-bit of Rs * Rt
    # hi = higher 32-bit of Rs * Rt
Division
  div Rs, Rt # lo = quotient of Rs/Rt
    # hi = remainder of Rs/Rt
Moves the contents of lo/hi registers to GPR (General Purpose Register)
  mflo $2 # $2 = lo
  mfhi $3 # $3 = hi

## Slide 80: Machine Code of Mult/Div/Mflo/Mfhi
Mult/Div/Mflo/Mfhi
  Example:
    mult $5, $4
    div $5, $4
    mflo $5
    mfhi $4
Opcode
Rs
6 bits
5 bits
Rt
5 bits
Rd
5 bits
Shamt
5 bits
Function
6 bits
32 bits
000000
00101
00100
00000
00000
0x18
000000
00101
00100
00000
00000
0x1a
000000
00000
00000
00101
00000
0x12
000000
00000
00000
00100
00000
0x10

## Slide 81: J-Type Instruction
There is another type, J, in MIPS for Jump instruction
  Similar to unconditional branch
  j target # Jump to target
Opcode
Target
6 bits
26 bits
32 bits

## Slide 82: Jump Target Addressing
Jump instruction provides larger scale jump than branch
Target address = First 4 bits of jump’s next instruction address : Last 28 bits of (target x 4)
Example: j Loop (0x00080000)
  The first 4 bits of Exit = 0x0
  Last 28 bits of target x 4 = 0080000
  target field = 0x0020000
00080000 | Loop: sll $t1, $s3, 2
00080004 | add $t1, $t1, $s6
00080008 | lw $t0, 0($t1)
0008000C | bne $t0, $s5, Exit
00080010 | addi $s3, $s3, 1
00080014 | j Loop
00080018 | Exit: …
00
Target
PC [31:28]
Target address of Jump
4-bits
26-bits
2-bits
32 bits
A good, detailed explanation:
https://chortle.ccsu.edu/assemblytutorial/Chapter-17/ass17_5.html

## Slide 83: Machine Code of J-Type Instructions
Jump in J-Type machine code format
  Example:
    j Loop
000010
00000000000000100000000000000000
0x0020000
0x2
Opcode
Target
6 bits
26 bits
32 bits

## Slide 84: Loops in MIPS: While Loops
Loop code consists of
  Condition check code
    To decide to continue the loop iteration or exit
  Jump to the loop entry to run the next iteration
  Example: Find x where 2x = 128
int pow = 1;
int x = 0;
while (pow != 128)
{
pow = pow * 2;
x = x + 1;
}
# $s0 = pow, $s1 = x
addi $s0, $0, 1
add $s1, $0, $0
addi $t0, $0, 128
while: beq $s0, $t0, done
sll $s0, $s0, 1
addi $s1, $s1, 1
j while
done:
MIPS
High-level language

## Slide 85: Loops in MIPS: For Loop
Loop code consists of
  Condition check code
    To decide to continue the loop iteration or exit
  Jump to the loop entry to run the next iteration
  Example: Add numbers from 0 to 9
int sum = 0;
int i;
for (i = 0; i != 10; i++)
{
sum = sum + i;
}
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
MIPS
High-level language

## Slide 86: Less Than Comparisons
The previous for loop can be rewritten by using “less than” operation like below
  Example: Add numbers from 0 to 9
int sum = 0;
int i;
for (i = 0; i < 10; i++)
{
sum = sum + i;
}
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
MIPS
High-level language
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:

## Slide 87: Less Than Comparisons
To reduce the number of instructions, you can also use slti or sltui instead of slt
  Example: Add numbers from 0 to 9
int sum = 0;
int i;
for (i = 0; i < 10; i++)
{
sum = sum + i;
}
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
addi $t0, $0, 10
for: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
MIPS
High-level language
# $s0 = i, $s1 = sum
add $s0, $0, $0
add $s1, $0, $0
for: slti $t1, $s0, 10
beq $t1, $0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
  slti Rt, Rs, imm # if (Rs < imm) Rt = 1; else Rt = 0;

## Slide 88: Calling a Subroutine
How are subroutines executed?
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
How can we jump back to the Caller function,
and resume the execution from the immediate
following line of the subroutine calling line?
We should record the return address before
jumping to the subroutine

## Slide 89: Special Registers
Assembler Name | Register Number | Description
$zero | $0 | Constant 0 value
$at | $1 | Assembler temporary
$v0-$v1 | $2-$3 | Function return values
$a0-$a3 | $4-$7 | Function Arguments
$t0-$t7 | $8-$15 | Temporaries
$s0-$s7 | $16-$23 | Saved Temporaries
$t8-$t9 | $24-$25 | Temporaries
$k0-$k1 | $26-$27 | Reserved for OS kernel
$gp | $28 | Global Pointer (Global and static variables/data)
$sp | $29 | Stack Pointer
$fp | $30 | Frame Pointer
$ra | $31 | Return Address
$ra register holds the return address

## Slide 90: Jump and Link Instruction
Most of assembly languages provide a special jump (or branch) instruction that Jump + Update Return Address Register
  JAL Label 1. Jump to Label and
  2. Update $ra with return address
  (JAL’s next instruction address)
Jump and Link
Target code line to jump

## Slide 91: Calling a Subroutine
How can we jump back to address in $ra?
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
jal sub_func
$pc  address of first line of sub_func
$ra  address of a += b;

## Slide 92: Jump with Register
We can return to the Caller by running Jump with Register instruction with $ra as an operand
  JR $ra # Jump to address in $ra
  # ($pc = $ra)
Jump with Register
Register holding the jump target address

## Slide 93: Jump with Register
Assume that the addresses in the previous example are like below
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
jal sub_func
$pc  address of first line of sub_func
$ra  address of a += b
0x00000160
0x00000200
0x00000204
0x00000208
0x00000208
0x000001600
jr $ra
$pc  $ra

## Slide 94: Jump with Register
Assume that the addresses in the previous example are like below
int sub_func(void) { … } int main () { a = 1; b = sub_func(); a += b; }
jal sub_func
$pc  address of first line of sub_func
$ra  address of a += b
0x00000160
0x00000200
0x00000204
0x00000208
0x00000208
0x000001600
jr $ra
$pc  $ra
0x000002080
Return to the return address in $ra

## Slide 95: Exercise
Translate the given high-level language code to MIPS assembly.
  Assume that the address of integer variable x and y are in $4 and $1 respectively.
if (x > y)
x = x + y; else x = 1;
High-level language
Tasks to do:
Load x value to a register
Load y value to another register
Check if y is less than x
If true, run add operation
Else, store 1 to one register
Store the result value to x in memory

## Slide 96: Exercise
Translate the given high-level language code to MIPS assembly.
  Assume that the address of integer variable x and y are in $4 and $1 respectively.
lw $2, 0($4)
lw $3, 0($1)
slt $1, $3, $2
beq $1, $0, Else
add $2, $2, $3
addi $2, $0, 1
if (x > y)
x = x + y; else x = 1;
MIPS
High-level language
Tasks to do:
Load x value to a register
Load y value to another register
Check if y is less than x
If true, run add operation
Else, store 1 to one register
Store the result value to x in memory
If false, you should
not execute add
 Create a label for else case and branch
Else:

## Slide 97: Exercise
Translate the given high-level language code to MIPS assembly.
  Assume that the address of integer variable x and y are in $4 and $1 respectively.
lw $2, 0($4)
lw $3, 0($1)
slt $1, $3, $2
beq $1, $0, Else
add $2, $2, $3
b Next
addi $2, $0, 1
sw $2, 0($4)
if (x > y)
x = x + y; else x = 1;
MIPS
High-level language
Tasks to do:
Load x value to a register
Load y value to another register
Check if y is less than x
If true, run add operation
Else, store 1 to one register
Store the result value to x in memory
Else:
Wait, when x > y, the calculation result should be also stored to the memory without executing the else code
 Add unconditional branch and skip addi
x > y
x <= y
Next:

## Slide 98: Parameter Passing
How can we pass the parameters to/from a subroutine?
int sub_func(int a) { … } int main () { a = 1; b = sub_func(c); a += b; }
Input parameter “c” should be passed
Output “b” should be returned

## Slide 99: Registers For Parameter Passing
Input Parameters
  Up to 4 parameters in $a0 ~ $a3
  If more than 4 parameters, use stack from 5th parameter
Return Value
  For 32-bit return value, $v0 is used
  $v1 also is used when the return value is 64 bits long
    i.e. $v0 holds the bottom 32 bits and $v1 holds the top 32 bits

## Slide 100: Example
int t;
int main(void) {
int y;
…
y = diffofsums(2, 3, 4, 5);
…
}
int diffofsums (int f, int g, int h, int i) {
int result;
result = (f + g) – (h + i);
return result;
}
High-level language
main:
…
addi $a0, $0, 2 # arg 0 = 2
addi $a1, $0, 3 # arg 1 = 3
addi $a2, $0, 4 # arg 2 = 4
addi $a3, $0, 5 # arg 3 = 5
jal diffofsums # call subroutine
add $s0, $v0, $0 # y = returned value
…
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
MIPS Assembly

## Slide 101: Example (Addressing)
Question: What values the following registers will have in each condition?
After jal
  $pc : 0x00000168
  $ra : 0x00000160
After jr
  $pc : 0x00000160
Address
0x0000015C
0x00000160
0x00000168
.
.
.
0x0000016E
main:
…
addi $a0, $0, 2 # arg 0 = 2
addi $a1, $0, 3 # arg 1 = 3
addi $a2, $0, 4 # arg 2 = 4
addi $a3, $0, 5 # arg 3 = 5
jal diffofsums # call subroutine
add $s0, $v0, $0 # y = returned value
…
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
MIPS Assembly

## Slide 102: Register Value Overwriting
Register file is a shared resource
Example:
  In the previous code, $t0, $t1, and $s0 are updated by Callee
  Assume that main function wanted to compare the diffofsums return value with value 10 and $t0 has value 10 before calling subroutine
  After calling the subroutine, $t0 is updated with intermediate compute result  incorrect comparison
main:
…
addi $t0, $0, 10 # main wanted to use $t0
addi $a0, $0, 2 # arg 0 = 2
addi $a1, $0, 3 # arg 1 = 3
addi $a2, $0, 4 # arg 2 = 4
addi $a3, $0, 5 # arg 3 = 5
jal diffofsums # call subroutine
add $s0, $v0, $0 # y = returned value
slt $t1, $s0, $t0 # to compare with comp result
…
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
After returning from diffofsums, main function will see the values of $t0, $t1, and $s0 are updated unexpectedly

## Slide 103: Register Value Overwriting
Use Stack memory to protect register values
  Callee backs up the values of registers to stack memory that will be updated in its function body
  Callee restores the values from stack to original registers before returning to Caller
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller

## Slide 104: Register Value Overwriting
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller
Compiled machine code
…
$t0 (10)
$t1 (2)
…
$ra
Register File
$s0 (9)
Stack region
allocation for
diffofsums
…
…
$sp
9
10
2
$t0 (5)
$t1 (9)
$s0 (-4)
After computations
in the function, registers are updated

## Slide 105: Register Value Overwriting
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + I
sub $s0, $t0, $t1 # result = (f + g) – (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller
Compiled machine code
…
$t0 (10)
$t1 (2)
…
$ra
Register File
$s0 (9)
Stack region
allocation for
diffofsums
…
…
$sp
9
10
2
$t0 (5)
$t1 (9)
$s0 (-4)
Before returning to Caller,
Register values are revoked

## Slide 106: Example: Nested Function Call
func1:
addi $sp, $sp, -4 # make space on stack
# to store $ra register
sw $ra, 0($sp) # save $ra on stack
jal func2 # jump to func2
…
lw $ra, 0($sp) # restore $ra from stack
addi $sp, $sp, 4 # deallocate stack space
jr $ra # return to caller
func2:
addi $sp, $sp, -8 # make space on stack
# to store 2 registers
…
addi $sp, $sp, 8 # deallocate stack space
jr $ra # return to func1 (caller)
Compiled machine code
…
Used by func1
Used by func2
Used by func2
$sp before func1
$sp in func1
$sp in func2
Why does func1 store $ra in stack before calling func2?

## Slide 107: Example: Recursion
Recursive functions should keep its input parameters and return address to the stack because all the recursions will try to use the same registers for these.
Int factorial (int n)
{
if (n <= 1)
return 1;
else
return (n * factorial (n-1));
}
High-level language
MIPS Assembly
factorial: addi $sp, $sp, -8 # make room
sw $a0, 4($sp) # store input (n)
sw $ra, 0($sp) # store return address
addi $t0, $0, 2 # $t0 = 2
slt $t0, $a0, $t0 # n <= 1?
beq $t0, $0, else # no: go to else (recursion)
addi $v0, $0, 1 # yes: return 1
addi $sp, $sp, 8 # restore $sp
jr $ra # return
else: addi $a0, $a0, -1 # n = n -1
jal factorial # recursive call
lw $ra, 0($sp) # restore return address
lw $a0, 4($sp) # restore input
addi $sp, $sp, 8 # restore $sp
mul $v0, $a0, $v0 # n * factorial(n-1)
jr $ra # return

## Slide 108: Example: Recursion for 3!
Compiled machine code
…
$sp
0x000000FC
0x000000F8
0x000000F4
0x000000F0
0x000000EC
0x000000E8
0x000000E4
0x000000E0
0x000000DC
…
$a0 (0x3)
$ra
$sp
$a0 (0x2)
$ra
$sp
$a0 (0x1)
$ra
factorial: addi $sp, $sp, -8 # make room
sw $a0, 4($sp) # store input (n)
sw $ra, 0($sp) # store return address
addi $t0, $0, 2 # $t0 = 2
slt $t0, $a0, $t0 # n <= 1?
beq $t0, $0, else # no: go to else (recursion)
addi $v0, $0, 1 # yes: return 1
addi $sp, $sp, 8 # restore $sp
jr $ra # return
else: addi $a0, $a0, -1 # n = n -1
jal factorial # recursive call
lw $ra, 0($sp) # restore return address
lw $a0, 4($sp) # restore input
addi $sp, $sp, 8 # restore $sp
mul $v0, $a0, $v0 # n * factorial(n-1)
jr $ra # return
$sp
$v0 = 1
$sp
$a0 = 2
$v0 = 2 x 1
$sp
$a0 = 3
$v0 = 3 x 2
$v0 = 6

## Slide 109: Exercise 1
Translate the given high-level language code to MIPS assembly
  Assume that the base address of an integer array a is in register $s0
    base address of an array: the address of the first element of the array
a[1]++;
lw $t3, 4($s0)
addi $t3, $t3, 1
sw $t3, 4($s0)
MIPS
High-level language
a[0]
a[1]
a[2]
Address
of a[0] is in $s0
in this exercise
0x7000
0x7004
0x7008
If you defined int a[3]; and the system allocated
a chunk of memory for this 3-element array from 0x7000,
the address of elements would be like below
Memory allocation for Arrays
4 byte (integer)

## Slide 110: Exercise 2
Translate the given high-level language code to MIPS assembly
  Assume that the base address of a char array a is in register $s0
    base address of an array: the address of the first element of the array
  Assume that the value of i is in $t0.
a[i]--;
MIPS
High-level language
a[0]
Address
of a[0] is in $s0
in this exercise
0x7000
0x7004
If you defined char a[8]; and the system allocated
a chunk of memory for this 8-element array from 0x7000,
the address of elements would be like below
Memory allocation for Arrays
1 byte (char)
a[1]
a[2]
a[3]
a[4]
a[5]
a[6]
a[7]

## Slide 111: Exercise 2
Translate the given high-level language code to MIPS assembly
  Assume that the base address of a char array a is in register $s0
    base address of an array: the address of the first element of the array
  Assume that the value of i is in $t0.
a[i]--;
add $t2, $s0, $t0
lb $t3, 0($t2)
subi $t3, $t3, 1
sb $t3, 0($t2)
MIPS
High-level language
Now we know that the address of a[i] is $s0 + 1byte * i = $s0 + $t0
Is this a valid operation to get one byte from $s0 + $t0?
lb $t1, $t0($s0)
No, because offset should be an immediate value, not a register id
We should change the base address value, not offset value
i.e. new base: $t2 = $s0 + $t0
and then load one byte from 0($t2)