## Slide 1
Pipelining
Lishan Yang
GMU CS695
Advanced Computer Architecture
Spring 2023
Notre Dame Cathedral

## Slide 2
Pipelining
Lishan Yang
GMU CS695 Advanced Computer Architecture
Spring 2023
Lecture 3
Reference:
CMPE 140, Hyeran Jeon
CMPE 140, Donald Hung
CMPE 140, Haonan Wang
Computer Architecture: A Quantitative Approach
Licensed for use under a Creative Commons Attribution-NonCommercial-ShareAlike 3.0 Unported License.

## Slide 3: Instruction Processing
CPU
A 32-bit instruction
Decoder
The instruction is
- Opcode: add
- Rs: $4
- Rt: $3
- Rd: $5
Compiled machine code
Return address
*fp
size
sum
numbers[1]
numbers[0]
add*
Value of $4
Value of $3
Calculated result
To be stored to $5
Instruction Processing

## Slide 4: Instruction Execution on CPU
To run a software, CPU
  (IF) Fetches instructions from memory in the right order
  (ID) Decodes the instruction and Reads the operand values from register file
  (EXE) Executes the computation by using ALU
  (MEM) Loads/store data from/to memory
  (WB) Writes back the computation results to register file
Instruction Fetch
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register

## Slide 5: Single-Cycle CPU Performance Analysis
The longest instruction’s execution time is 925 ps.
If we run 100 billion instructions, what is the total execution time?
The clock cycle period should be set to 925 ps
CPU time = # instructions x CPI x cycle period
= 100 x 109 x 1 x 925 x 10-12
= 92.5 seconds

## Slide 6: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Violates design principle
  Making the common case fast
  More arithmetic operations than memory operations
Most modern CPUs use multi-cycle processors
  Each instruction takes multiple cycles
  Multiple instructions can execute concurrently (parallelism  pipelining)

## Slide 7: Pipelining Analogy
Laundry tasks
  Place one dirty load of clothes in the washer
  Place the wet load in the dryer
  Place the dry load on a table and fold
  Ask your roommate to put the clothes away

## Slide 8: Pipelining Analogy
Laundry tasks
  Place one dirty load of clothes in the washer
  Place the wet load in the dryer
  Place the dry load on a table and fold
  Ask your roommate to put the clothes away

## Slide 9: Pipelining Analogy
Lots of dirty clothes -- need to wash them over four separate loads
Assume each task takes 30 minutes
Inefficient!

## Slide 10: Pipelining Analogy
You can start the next load as soon as the washer finishes washing the previous load
Saved 4.5 hours

## Slide 11: Pipelining Analogy
We can parallelize the single-cycle CPU tasks in a similar way
Pipelined laundry  overlapping execution
Pipelined CPU
clock cycle period = 0.5hrs
Single-cycle CPU
clock cycle period = 2hrs

## Slide 12
5 steps in one cycle for single-cycle CPU design
  With each step using separate resources
Instruction Fetch
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register
CLK
IF
ID
EXE
MEM
WB

## Slide 13: MIPS Pipeline (Five-stage pipeline)
Entire datapath can be broken into five stages
Cycle period is changed to the time taken for a stage
  Shorter clock cycle
  Higher CPI (e.g., CPI = 5 in MIPS)
CLK
Instruction Fetch
Decode & Register
Identify opcode & read operands
Execute
Mem
Write Result
Write to
dst register
IF
ID
EXE
MEM
WB

## Slide 14: MIPS Pipeline (Five-stage pipeline)
Entire datapath can be broken into five stages
Cycle period is changed to the time taken for a step
  Shorter clock cycle
  Higher CPI (e.g., CPI = 5 in MIPS)
  System can achieve CPI = 1 by overlapping Multiple Instructions
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
Inst1 | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
Inst2 |  | IF | ID | EXE | MEM | WB |  |  |  |  | 
Inst3 |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
Inst4 |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Inst5 |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
CC: clock cycle
After initial pipeline filling phase,
we can finish an instruction every cycle
Initial pipeline filling phase

## Slide 15: Pipeline Performance Example
100ps for register IOs (i.e., decode, writeback); 200ps for other stages
What would be the cycle period in single-cycle and pipelined datapath?
What would be the execution time of lw instruction?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-type | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 16: Pipeline Performance Example
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Tc = Longest instruction
Tc = Longest Stage
Tlw = 800ps
Tlw = 1000ps
2 x Tlw = 1600ps
2 x Tlw = 1200ps
…
…

## Slide 17: Throughput
Pipeline IPC | 
Let (n = infinity) | 
Pipeline IPC | 
Throughput (T) = # of instructions executed / time
IPC = Instruction Per Cycle = 1 / CPI
  For a large number of instructions, the IPC of a pipelined processor is 1 instruction per clock cycle
  Only when we keep the pipeline full of instructions
Assume we execute N instructions using a K stage datapath
CPI: Cycle per instruction
- The smaller the better
IPC: Instruction per cycle
- The larger the better

## Slide 18: Hazards
Any sequence of instructions that prevent full pipeline utilization
  Often causes the pipeline to stall for one or more instructions
Structural Hazards
  HW organization cannot support certain combinations of instructions being overlapped
Data Hazards
  Data dependencies
Control Hazards
  Branches & changes to PC in the pipeline
  If branch is determined to be taken later in the pipeline, flush (delete) the instructions in the pipeline that shouldn’t be executed
Hardware (not homework!)

## Slide 19: Structural Hazards
Combinations of instructions that cannot be overlapped in the given order due to HW constraints
  Often due to lack of HW resources
Example: A single memory rather than separate I & D Memories
  Structural hazard whenever an instruction needs to perform a data access (i.e. ‘lw’ or ‘sw’)
Memory
ALU
Reg.
File
PC
LW
i+2
i+1
i
Hazard!
IF: fetch the instruction, write to memory
…
MEM: write the data to memory
This is not a good design :(
Fix:
Instruction cache (ICache)
Data cache (DCache)

## Slide 20: Data Hazards
Read-After-Write (RAW)
  A following instruction reads a result from a previous instruction
Write-After-Read (WAR)
Write-After-Write (WAW)
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4
Initial Conditions:
$s0 = 0x10010000
$t1 = 0x0
$t4 = 0x24
After execution values should be:
$t5 = 0x0
00000060
12345678
0x10010000
0x10010004
$s0 = 0x10010000
$t1 = 0x60
$t4 = 0x24
$t5 = 0x84

## Slide 21: Cause of Data Hazards
Stalling the pipeline to prevent error:
  All instructions in front of the stalled instruction can continue
  All instructions behind the stalled instruction must also stall
Stalling inserts “bubbles” / nops (no-operations) into the pipeline
  A “nop” is an actual instruction in the MIPS ISA that does NOTHING

## Slide 22: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF |  |  |  |  |  |  |  |  |  | 
ADD |  |  |  |  |  |  |  |  |  |  | 
Next instr. |  |  |  |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 23: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID |  |  |  |  |  |  |  |  | 
ADD |  | IF |  |  |  |  |  |  |  |  | 
Next instr. |  |  |  |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 24: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 25: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
Hazard
Dependency detected (ADD cannot do EXE because $t1 is not ready)
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 26: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
nop
nop
Stays in ID stage
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 27: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
ADD |  | IF | ID |  |  |  |  |  |  |  | 
Next instr. |  |  | IF |  |  |  |  |  |  |  | 
Next+1 |  |  |  |  |  |  |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
nop
nop
nop
nop
Read new value again
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 28: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  | 
ADD |  | IF | ID |  |  | EXE |  |  |  |  | 
Next instr. |  |  | IF |  |  | ID |  |  |  |  | 
Next+1 |  |  |  |  |  | IF |  |  |  |  | 
Next+2 |  |  |  |  |  |  |  |  |  |  | 
Next+3 |  |  |  |  |  |  |  |  |  |  | 
Next+4 |  |  |  |  |  |  |  |  |  |  | 
nop
nop
nop
nop
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 29: Data Hazards Example
Using stalls to handle dependencies
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC13
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  | EXE | MEM | WB |  |  |  |  | 
Next instr. |  |  | IF |  |  | ID | EXE | MEM | WB |  |  |  | 
Next+1 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+2 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+3 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+4 |  |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB
nop
nop
nop
nop
Throughput = 7 insts/13 cycles = 0.53
vs.
Throughput without hazard = 7 insts/11 cycles = 0.63
RAW Example
  LW $t1,4($s0)
  ADD $t5,$t1,$t4

## Slide 30: Pipeline Stall for Data Hazards
ADD can read the updated register value from the register file in the same cycle as LW writes the loaded data to register
Do we really need to wait until LW updates the register file?
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC13
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID |  |  | EXE | MEM | WB |  |  |  |  | 
Next instr. |  |  | IF |  |  | ID | EXE | MEM | WB |  |  |  | 
Next+1 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+2 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+3 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+4 |  |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB
nop
nop
nop
nop
Why don’t we use this data directly?

## Slide 31: Data Hazards Solutions
Compiler
  Reorder Code
Hardware
  Use forwarding / bypassing
Data forwarding
  Take results still in the pipeline (not yet written back to a register) and pass them to dependent instructions
  Forwarding Path
    Load instruction: from WB to EXE
    R-type instructions: from MEM to EXE

## Slide 32: Data Forwarding
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10 | CC11 | CC12 | CC13
LW | IF | ID | EXE | MEM | WB |  |  |  |  |  |  |  | 
ADD |  | IF | ID | ID | EXE | MEM | WB |  |  |  |  |  | 
Next instr. |  |  | IF | IF | ID | EXE | MEM | WB |  |  |  |  | 
Next+1 |  |  |  |  | IF | ID | EXE | MEM | WB |  |  |  | 
Next+2 |  |  |  |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+3 |  |  |  |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+4 |  |  |  |  |  |  |  | IF | ID | EXE | MEM | WB | 
Saved 1 cycles
compared to w/o forwarding
Only one stall to wait for LW reads data from memory
nop
nop

## Slide 33: Data Forwarding
As far as earlier instruction’s result is in pipeline, the result value can be forwarded to the following instructions
In arithmetic operations, no stall is needed
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
ADD | IF | ID | EXE | MEM | WB |  |  |  |  | 
SUB |  | IF | ID | EXE | MEM | WB |  |  |  | 
XOR |  |  | IF | ID | EXE | MEM | WB |  |  | 
Next+1 |  |  |  | IF | ID | EXE | MEM | WB |  | 
Next+2 |  |  |  |  | IF | ID | EXE | MEM | WB | 
Next+3 |  |  |  |  |  | IF | ID | EXE | MEM | WB
ADD $t3,$t1,$t2
SUB $t5,$t3,$t4
XOR $t7,$t5,$t3

## Slide 34: Pipeline Latency with Forwarding/Stall
Number of cycles we must stall to execute a dependent instruction:
Instruction that is the dependency source | w/o Forwarding (cycles) | w/ Forwarding (cycles)
LW | 2 | 1
Other instructions that update register file | 2 | 0
Data Hazards Solutions:
  - Hardware: stalling & forwarding
  - Software: compiler -- code reordering/rescheduling

## Slide 35: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Find RAW dependencies and check if stall is needed

## Slide 36: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
When forwarding is used,
only lw instruction causes stall
Leave lw instructions only
Find RAW dependencies and check if stall is needed

## Slide 37: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Find RAW dependencies and check if stall is needed
lw instructions cause 1-cycle stalls
Leave instructions that are executed back-to-back only

## Slide 38: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Now, check if the lw and dependent instructions must be executed back-to-back

## Slide 39: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)

## Slide 40: Code Scheduling to Avoid Stalls
Compiler can reorder code to avoid the stalls
C code A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
5 cycles for the first inst +
6 cycles for the remaining insts +
2 x 1 stall cycles = 13 cycles
Total
execution time
5 cycles for the first inst +
6 cycles for the remaining insts +
0 stall cycles = 11 cycles

## Slide 41: Control Hazard
Branch outcomes: Taken (T) or Not-Taken (NT)
Not known until late in the pipeline
  Prevents us from fetching future instructions
  Solution: rather than stall, we can predict the outcome and keep fetching
  We only need to correct the pipeline if we guess wrong
Static Predictions
  Predict Taken
  Predict Not Taken
--- beq L1 L2 --- --- --- --- beq L2 L1 ---
T
T
NT
NT

## Slide 42: Statically Predict Not Taken
Keep fetching instructions from the PC + 4 by assuming that the branch will be not taken
Once branch is turned out to be taken, flush the incorrectly fetched instructions
In the following cycle, fetch the instruction from the branch target address

## Slide 43: Static Branch Prediction Penalty
Penalty = number of instructions that need to be flushed on misprediction
For static branch prediction:
  The branch outcome and target address is available at the MEM stage and passed back to the Fetch stage
  If mispredicted, instructions of the correct path will be fetched on the next cycle
A 3-cycle branch penalty when mispredicted

## Slide 44: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM |  |  |  |  |  | 
ADD |  | IF | ID | EXE |  |  |  |  |  | 
SUB |  |  | IF | ID |  |  |  |  |  | 
OR |  |  |  | IF |  |  |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
NT!

## Slide 45: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM |  |  |  |  | 
SUB |  |  | IF | ID | EXE |  |  |  |  | 
OR |  |  |  | IF | ID |  |  |  |  | 
BNE |  |  |  |  | IF |  |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 46: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 47: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM |  | 
AND |  |  |  |  |  | IF | ID | EXE |  | 
SW |  |  |  |  |  |  | IF | ID |  | 
LW |  |  |  |  |  |  |  | IF |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!
Flush

## Slide 48: Statically Predict Not Taken
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF | ID | EXE |  | 
SW |  |  |  |  |  |  | IF | ID |  | 
LW |  |  |  |  |  |  |  | IF |  | 
ADD |  |  |  |  |  |  |  |  | IF | ID
SUB |  |  |  |  |  |  |  |  |  | IF
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
nop
nop
nop
nop

## Slide 49: Predict Taken?
It is not possible to statically predict all the branches to be taken
  The branch target address is not computed until the EX stage, so we don’t have the PC values even needed to predict taken
Dynamic branch prediction + branch target buffer enables to predict taken
  Predict untaken a few times to collect branch target address of each branch and then predict taken based on the history
Can we reduce branch penalty with change of datapath?

## Slide 50: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!
Flush

## Slide 51: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF |  |  |  | 
ADD |  |  |  |  |  |  | IF | ID | EXE | MEM
SUB |  |  |  |  |  |  |  | IF | ID | EXE
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
T!
Flush
nop
nop

## Slide 52: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM |  |  |  | 
OR |  |  |  | IF | ID | EXE |  |  |  | 
BNE |  |  |  |  | IF | ID |  |  |  | 
AND |  |  |  |  |  | IF |  |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome

## Slide 53: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM |  |  | 
BNE |  |  |  |  | IF | ID | ID |  |  | 
AND |  |  |  |  |  | IF | IF |  |  | 
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
T!

## Slide 54: Early Determination w/ Predict NT
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | ID | EXE | MEM | WB
AND |  |  |  |  |  | IF | IF |  |  | 
ADD |  |  |  |  |  |  |  | IF | ID | EXE
SUB |  |  |  |  |  |  |  |  | IF | ID
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $s0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
nop
T!
If BNE has dependency with its preceding instruction, OR, one cycle stall is required to get the OR’s result value
 Still better than normal 3 cycle flushing
What about a LW here?
What about NT here?

## Slide 55: Branch Delay Slot
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
OR |  |  |  | IF | ID | EXE | MEM | WB |  | 
BNE |  |  |  |  | IF | ID | EXE | MEM | WB | 
AND |  |  |  |  |  | IF |  |  |  | 
ADD |  |  |  |  |  |  | IF | ID | EXE | MEM
SUB |  |  |  |  |  |  |  | IF | ID | EXE
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
OR $s0,$t6,$t7
BNE $a0,$s1,L2 (T)
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
nop
nop
T!
Flush
nop
nop
Find an instruction that
1) has to be executed regardless branch outcome
2) independent to branch
The instruction will be placed in the branch delay slot (right after branch instruction) instead of fetching wrong instruction and flushing

## Slide 56: Branch Delay Slot
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
BEQ | IF | ID | EXE | MEM | WB |  |  |  |  | 
ADD |  | IF | ID | EXE | MEM | WB |  |  |  | 
SUB |  |  | IF | ID | EXE | MEM | WB |  |  | 
BNE |  |  |  | IF | ID | EXE | MEM | WB |  | 
OR |  |  |  |  | IF | ID | EXE | MEM | WB | 
ADD |  |  |  |  |  | IF | ID | EXE | MEM | WB
SUB |  |  |  |  |  |  | IF | ID | EXE | MEM
BEQ $a0,$a1,L1 (NT)
L2: ADD $s1,$t1,$t2
SUB $t3,$t0,$s0
BNE $a0,$s1,L2 (T)
OR $s0,$t6,$t7
L1: AND $t3,$t6,$t7
SW $t5,0($s1)
LW $s2,0($s5)
Actual Branch Outcome
Instruction in the
target address (L2)
No Flush
& Better Performance

## Slide 57: Branch Delay Slot
Require implementation on both the CPU and the compiler
  If no suitable instruction can be found for the slot, then a NOP will be filled
Branch delay slot is more useful for unconditional branches such as j, jal, jr because they are always taken
For example, if jal uses branch delay slot,
  After jal, $ra is updated with PC + 8
  The instruction in PC + 4 is executed after jal before entering the subfunction

## Slide 58: Dynamic Branch Prediction
Monitor the branch patterns for better prediction
  i.e. loops usually have a few iterations, so the branch in the loop is likely to be not taken at least for a few times
Branch Prediction Buffer (branch history buffer) is used to maintain each branch’s outcome history
  Small storage space indexed with certain bits of branch instruction’s PC value
  Each entry maintains the previous outcome of each branch
  Once the branch outcome is available, the corresponding entry is updated

## Slide 59: Branch Prediction Buffer
Aliasing issue
  Different branch instructions may map to the same branch prediction buffer entry if their PC values have the same LSBs, affecting each others’ predictions
    E.g., 0x8004 and 0x8104 will access the same entry if [3:2] bits are used for indexing
    Inevitable but can be alleviated with larger buffer
1000 0000 0000 0100
Branch instruction’s PC value (i.e. 0x8004)
[3:2] bits
 | prediction bit
0 | 1
1 | 0
2 | 1
3 | 1
Branch Prediction Buffer
The bits to be included to the prediction
may be different depending on the prediction buffer size
1: Predict Taken
0: Predict Not Taken
Prediction bit field can have multiple bits to record more history
 PC can be recorded to predict Taken

## Slide 60: 1-bit Predictor
Each entry of branch prediction buffer is 1-bit (1: Taken, 0: Not Taken)
  The entry value is the latest outcome of the branch
  Next outcome of the branch is predicted based on current value
  Example: Assume that the actual outcomes of the branches at 0xDC04, 0xDC08, and 0xDC20 are untaken, taken, and untaken, respectively
0xDC04 for(i=0;i<10000;i++)
{
0xDC08 if( ( i % 100) == 0 )
tick( );
0xDC20 if( (i % 2) == 0)
even();
}
prediction bit
0
1
0
..
predicted T
predicted NT
predicted NT
Actual result: NT
0
Actual result: NT
1
Actual result: T

## Slide 61: Is 1 bit Enough?
DC04: NNNNNNN ... NNNNNNNNNNT
10,000 iterations
Mis-predictions: 2 / 10,000
NT
TN
DC08: TTTTT ... TNTTTTT … TNTTTTT …
Mis-predictions: 2 / 100
DC20: TNTNTNTNTNTNTNTNTNTNTNTNTNTNT …
Mis-predictions: 2 / 2
Mis-predictions for every
first and last iterations
 99.998% Correct Prediction
98.0% Correct Prediction
0.0% Correct Prediction
10,000 iterations …
NNNNNNNNN …
Not taken and continue to the loop body
Taken to exit the loop

## Slide 62: Using 2-bit History
2-bit Saturating Counter in each branch prediction buffer entry
  Could have more than two bits but two bits cover most patterns (i.e. loops)
0
1
FSM for 1-bit
Prediction
00
01
10
11
FSM for 2-bit
Saturating Counter
Predict NT
Predict T
Transition on T outcome
Transition on NT outcome

## Slide 63: Example
2
T

3
T
3
T


…
3
N

N
1

T
0

0
T
1
T
T
T
T
…
T
1
1
1
1






T
1

T
…
1

0
T
1
T
2
T
3
T
3
T
…
3
T






Initial Training/Warm-up
1-bit
Predictor
2-bit
Predictor
Only 1 Misprediction per N branches now!
Correct prediction rates:
DC04: 99.999% , DC08: 99.0%, DC20: 50%

## Slide 64: Pipelined CPU Performance Analysis
SPECINT2000 benchmark:
  25% loads, 10% stores, 11% branches, 2% jumps, 52% R-type
Assume:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
Average CPI calculation:
  Load/Branch CPI = 1 when no stalling, 2 when stalling
  CPIlw = 1(0.6) + 2(0.4) = 1.4
  CPIbeq = 1(0.75) + 2(0.25) = 1.25
  Overall average CPI = (0.25 x 1.4) + (0.1 x 1) + (0.11 x 1.25) + (0.02 x 2) + (0.52 x 1) = 1.15

## Slide 65: Pipelined CPU Performance Analysis
For a program with 100 billion instructions executing on the pipelined MIPS processor under discussion, execution time is
CPU time = # instructions x CPI x cycle time
= (100 x 109) x 1.15 x (550 x 10-12 sec)
= 63 seconds
Recall: when we ran the same code on a single-cycle processor (Lecture 4 – (3)), CPU time was 92.5 seconds.
Speedup of pipelined architecture = 92.5 / 63 = 1.47x