## Slide 1
Memory
Lishan Yang
GMU CS695
Advanced Computer Architecture
Spring 2023
Taj Mahal
IBM Power 7
Notes: http://netmgt.blogspot.com/2010/02/ibm-power-7-and-edram-cache.html

## Slide 2
Memory
Lishan Yang
GMU CS695 Advanced Computer Architecture
Spring 2023
Lecture 3
Reference:
CMPE 140, Hyeran Jeon
CMPE 140, Donald Hung
CMPE 140, Haonan Wang
Computer Architecture: A Quantitative Approach
Licensed for use under a Creative Commons Attribution-NonCommercial-ShareAlike 3.0 Unported License.

## Slide 3: Computer Architecture Overview
Instruction Set
Architecture
Software/Applications
Processor
Operating System
Firmware
Compiler
Registers
Cache
Memory
HDD/SSD
Memory Hierarchy

## Slide 4: Memory Hierarchy
#include <stdio.h>
#include <string.h>
int numbers[2];
void myfunction(void)
{
FILE *fp;
int size = 2;
int sum = 0;
/* Open file for reading */
fp = fopen(“mynumbers.txt", “r");
/* Read and display data */
fread(numbers, sizeof(int), size, fp);
fclose(fp);
sum = numbers[0] + numbers[1];
printf(“Sum = %d\n”, sum);
}
int main (void) {
myfunction();
return(0);
}
Example: a C program that reads
two integer values from “file.txt” file
and prints the sum of them.
Processor
(CPU)
Understands and executes each line of the code.
Uses fast on-chip memories
Memory
(DRAM)
Provides operands to CPU
(*fp, size, sum, numbers[2])
Storage
(HDD)
Provides file inputs and program code
(file.txt)

## Slide 5: Memory Hierarchy
On-chip Memories (Memories inside of CPU)
  Register file, Caches
  Small but Fast
CPU
Register File
Instruction
Cache
Data
Cache

## Slide 6: Memory Hierarchy
Off-chip Memories (Memories outside CPU)
  System Memory, Storage
  Large but Slow
System Memory
Storage
CPU

## Slide 7: Memory Hierarchy
Processor
Registers
Cache
Memory
HDD/SSD
Fast
Slow
Cheap
Expensive
Access
Speed
Price/unit
0.5ns ~ 2.5ns
$2000 ~ $5000 per GB
50ns ~ 200ns
$20 ~ $75 per GB
5ms ~ 20ms
$0.2 ~ $2 per GB
On-chip:
Subset of memory
Volatile Memory
Non-volatile Memory
(NVM)
Off-chip:
full memory
Software managed
1 register = 1 word
Hardware managed
1 block = multiple words

## Slide 8: Memories in Your PC
Windows
  This PC  Properties
  cmd window  wmic
  3rd party tool like CPU-Z
Linux
  lscpu
  cat /proc/cpuinfo
  etc.
System Memory
Storage
Caches

## Slide 9: Why?
Two Types of Locality:
  Temporal Locality (Locality in Time): If an address is referenced, it tends to be referenced again (e.g., loops, variable reuse)
  Spatial Locality (Locality in Space): If an address is referenced, neighboring addresses tend to be referenced (e.g., array, stack, etc.)
On-chip
Off-chip

## Slide 10: The “Memory Wall”
“Moore’s Law”
CPU ~55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Processor-Memory
Performance Gap (grows 50%/year)

## Slide 11: The Memory Hierarchy Goal
How do we create a memory system that gives the illusion of being large, cheap and fast (most of the time)?
  With hierarchy
    try the fast parts first -- most of the time, this works well
    if not, move the data so it works well the next time
  With parallelism
    use multiple identical parts operating simultaneously
    for large quantities of data, this works well
Example – keep a subset of the data in fast memory
Example – 1-byte-wide memory  4 × 1-byte-wide memory  4-byte-wide memory
  load word takes 4 memory cycles vs. 1 memory cycle

## Slide 12: Cache Design
Caches use SRAM for speed and technology compatibility
  Low density (6 transistor cells), high power, expensive, fast
  Static: content will last “forever” (until power turned off)
Example: A (2M X 16 bit) SRAM logic
Dout[15-0]
SRAM
2M x 16
Din[15-0]
Address
Chip select
Output enable
Write enable
16
16
21
> Read more:
https://en.wikipedia.org/wiki/Static_random-access_memory
https://en.wikipedia.org/wiki/Static_random-access_memory#/media/File:SRAM_Cell_(6_Transistors).svg

## Slide 13: SRAM Cache Design
r
o
w
d
e
c
o
d
e
r
row
address
4-bit data word
SRAM Cell
Array
word (row)
select line
bit (data) lines
Each intersection represents a
6-T SRAM cell
Column Selector &
I/O Circuits
column
address
Each row holds a data block
Column address selects the requested word from block

## Slide 14: Cache Hit and Miss
Hit: Data appears in some block of the cache
  Hit Rate: # hits / total accesses on the cache
  Hit Time: Time to access the cache
Miss: Data needs to be retrieved from the lower level (and stored in cache)
  Miss Rate: 1 - (Hit Rate)
  Miss Penalty: Average delay in the processor caused by each miss
Lower Level Memory
(cache/main memory)
Cache
To Processor
From Processor
data block X
data block Y
Can’t find!
Miss
Hit
Hit
read
read

## Slide 15: Memory Hierarchy Performance
Average Memory Access Time (AMAT)
= Hit Time + Miss rate x Miss Penalty
Example:
  Cache Hit = 1 cycle
  Miss rate = 10% = 0.1
  Miss penalty = 300 cycles
  AMAT = Thit(L1) + Miss_rate(L1) x T(Memory) = 1 + 0.1 x 300 = 31 cycles
Main
Memory
(DRAM)
First-level
Cache
Hit Time
Miss penalty
1 cycle
300 cycles
Due to long-latency memory, AMAT is 30 cycles longer than cache latency.
Can we reduce the overhead?

## Slide 16: Reducing Penalty: Multi-Level Cache
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 17: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x Miss_penalty(L1)
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 18: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x Miss_penalty(L2) ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 19: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x Miss_penalty(L3) } ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 20: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x T(memory) } ]
Main
Memory
(DRAM)
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Off-Chip

## Slide 21: Reducing Penalty: Multi-Level Cache
AMAT in multi-level cache organization
  = Thit(L1) + Miss_rate(L1) x
  [ Thit(L2) + Miss_rate(L2) x
  { Thit(L3) + Miss_rate(L3) x T(memory) } ]
Example:
  Miss rate of L1, L2, L3 = 10%, 5%, 1%, respectively
  AMAT = 1 + 0.1 x [ 10 + 0.05 x { 20 + 0.01 x 300 } ] = 2.115 cycles
Second
Level
Cache
Third
Level
Cache
300 cycles
20 cycles
10 cycles
On Processor Die
L1
L2
L3
First-level
Cache
Hit Time
1 cycle
Vs. 31 cycles
14.7x speedup!
Main
Memory
(DRAM)
Off-Chip
Are more levels always good?

## Slide 22: Discussion
Background: The cache space is limited. We can only keep a subset of data in cache.
Question: What happens when the cache is full?
Question: What to keep in the cache (which block should be evicted)?

## Slide 23: What to Keep in Caches?
It depends on the cache organization and replacing policy.
Cache organization:
  Cache line (block): The basic unit of data replacement. A longer cache line fetches and replaces more data per miss.
  Set: An entry that one cache line is mapped to according to certain bits of its address.
  Way: A slot within a cache set to hold one history cache line.
Way 0
Way 1
Set 0
Set 1
block 0
block 1
block 2
block 3
…
…

## Slide 24: What to Keep in Caches?
It depends on the cache organization and replacing policy
Cache line replacing policy: which history line should be replaced?
  In a set entry, each cache line can be identified with a Tag (a portion of its address).
  Least recently used (LRU), First-in first-out (FIFO), Random, etc.
Block offset
Byte offset
Index
Tag
Selects the set
Used for tag compare
Selects the word in the block
Data (e.g., 64 Bytes)
Tag
Valid
Address decoding:
Cache line:
History bits

## Slide 25: Cache Indexing
Block offset
Byte offset
Index
Tag
Selects the set
Used for tag compare
Selects the word in the block
Way 0
Way 1
Set 0
Set 1
Example: a simple 2-set x 2-way cache
block 0
block 1
block 2
block 3
Address decoding:

## Slide 26: Cache Types
N-way Set-Associative: Number of ways > 1 & Number of sets > 1
  Slightly complex searching mechanism
Direct Mapped: Number of ways = 1
  Fast indexing mechanism
Fully-Associative: Number of sets = 1
  Extensive hardware resources required to search
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative (only one set)
Direct mapped (only one way)
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Assuming fixed sized cache:
Way 0
Way 1
Set 0
Set 1
block 0
block 1
block 2
block 3
…
…

## Slide 27: MIPS Direct Mapped Cache Example
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
20
Data
32
Hit
  32bit address from the PC (Instr Fetch) or ALU (load, store addr)

## Slide 28: Multiword Block Direct Mapped Cache
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset

## Slide 29: Four-Way Set Associative Cache
31 30 . . . 11 10 9 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select

## Slide 30: Costs of Set Associative Caches
Must have hardware for replacement policy
  E.g., to keep track of when each way’s block was used
N-way set associative cache costs
  N comparators (delay and area) & MUX delay
    Data is available after Hit/Miss decision.
    In a direct mapped cache, the cache block is available before the Hit/Miss decision.
Total cache line size = valid field size + tag size + block data size + data for cache policy (e.g., time stamp, modified bit, etc.)

## Slide 31: Mapping Example: Direct Mapped
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block No.
in memory
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Set No.
in cache
12 % 8 = 4

## Slide 32: Mapping Example: Direct Mapped
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block No.
in memory
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Set No.
in cache
32

## Slide 33: Mapping Example: 2-way
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block No.
in memory
0 |  | 1 |  | 2 |  | 3 | 
Set No.
in cache
12 % 4 = 0
(can go anywhere in set 0)

## Slide 34: Mapping Example: 2-way
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block No.
in memory
0 |  | 1 |  | 2 |  | 3 | 
Set No.
in cache
34

## Slide 35: Mapping Example: Fully-associative
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block No.
in memory
Can go anywhere
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Way No.
in cache
35

## Slide 36: Mapping Example: Fully-associative
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block No.
in memory
Can go anywhere
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Way No.
in cache

## Slide 37: Miss Example 1: Direct Mapped
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
0 % 4 = 0
MEM[0]
Memory block 0 is not in the cache  MISS
CPU
Read 0
MEM[0]
MEM[8]
MEM[6]
MEM[5]

## Slide 38: Miss Example 1: Direct Mapped
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 8 is not in the cache  MISS
8 % 4 = 0
Cache block 0 is not empty
Evict MEM[0] and fetch MEM[8]
MEM[8]
CPU
Read 8
MEM[0]
MEM[8]
MEM[6]
MEM[5]

## Slide 39: Miss Example 1: Direct Mapped
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 0 is not in the cache AGAIN  MISS
0 % 4 = 0
MEM[8]
CPU
Read 0
MEM[0]
MEM[8]
MEM[6]
MEM[5]
Cache block 0 is not empty
Evict MEM[8] and fetch MEM[0]

## Slide 40: Miss Example 1: Direct Mapped
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
MEM[0]
Memory block 6 is not in the cache  MISS
6 % 4 = 2
MEM[8]
MEM[6]
MEM[6]
CPU
Read 6
MEM[5]

## Slide 41: Miss Example 1: Direct Mapped
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
MEM[0]
Memory block 5 is not in the cache  MISS
MEM[8]
MEM[6]
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
MEM[6]
CPU
Read 5
MEM[5]
5 % 4 = 1
MEM[5]

## Slide 42: Miss Example 2: Fully-associative
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 0 is not in the cache  MISS
CPU
Read 0
MEM[0]
MEM[8]
MEM[6]
MEM[5]
42

## Slide 43: Miss Example 2: Fully-associative
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 8 is not in the cache  MISS
CPU
Read 8
MEM[0]
MEM[8]
MEM[6]
MEM[8]
MEM[5]
43

## Slide 44: Miss Example 2: Fully-associative
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 0 is in the cache  HIT
CPU
Read 0
MEM[0]
MEM[8]
MEM[6]
MEM[8]
MEM[5]
44

## Slide 45: Miss Example 2: Fully-associative
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 6 is not in the cache  MISS
CPU
Read 6
MEM[0]
MEM[8]
MEM[6]
MEM[8]
MEM[6]
MEM[5]
45

## Slide 46: Miss Example 2: Fully-associative
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 5 is not in the cache  MISS
CPU
Read 5
MEM[0]
MEM[8]
MEM[6]
MEM[8]
MEM[6]
MEM[5]
MEM[5]
46

## Slide 47: Miss Example 2: Fully-associative
Memory block access sequence: 0, 8, 0, 6, 5, 4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 | 1 | 2 | 3
Block no.
in cache
MEM[0]
Memory block 4 is not in the cache  MISS
CPU
Read 4
MEM[0]
MEM[8]
MEM[6]
MEM[8]
MEM[6]
MEM[5]
MEM[5]
MEM[4]
Cache is full
Evict MEM[8] (LRU: least recently used)
and fetch MEM[4]
MEM[4]
47

## Slide 48: Miss Example 3: 2-way
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 |  | 1 | 
0 % 2 = 0
MEM[0]
Memory block 0 is not in the cache  MISS
CPU
Read 0
MEM[0]
MEM[8]
MEM[6]
Set no.
in cache
MEM[5]
48
Which data will be in the cache after accessing this sequence?

## Slide 49: Miss Example 3: 2-way
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 |  | 1 | 
8 % 2 = 0
MEM[0]
Memory block 8 is not in the cache  MISS
CPU
Read 8
MEM[0]
MEM[8]
MEM[6]
Set no.
in cache
MEM[8]
MEM[5]
49

## Slide 50: Miss Example 3: 2-way
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 |  | 1 | 
MEM[0]
Memory block 0 is in the cache  HIT
CPU
Read 0
MEM[0]
MEM[8]
MEM[6]
Set no.
in cache
MEM[8]
MEM[5]
50

## Slide 51: Miss Example 3: 2-way
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 |  | 1 | 
6 % 2 = 0
MEM[0]
Memory block 6 is not in the cache  MISS
CPU
Read 6
MEM[0]
MEM[8]
MEM[6]
Set no.
in cache
MEM[8]
MEM[6]
Cache set 0 is full
Evict MEM[8] (least recently accessed block)
and fetch MEM[6]
MEM[5]
51

## Slide 52: Miss Example 3: 2-way
Memory block access sequence: 0, 8, 0, 6, 5
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Block no.
in memory
0 |  | 1 | 
Memory block 5 is not in the cache  MISS
CPU
Read 5
MEM[0]
MEM[8]
MEM[6]
Set no.
in cache
MEM[0]
MEM[6]
MEM[5]
5 % 2 = 1
MEM[5]
52

## Slide 53: Cache Miss Classification: The 3 C’s
Compulsory (cold) Misses
  On the 1st reference to a block
  Related to # blocks accessed by a code, not related to the configuration of a cache
Capacity Misses
  The program’s working set size exceeds the cache capacity
Conflict Misses
  Multiple memory blocks map to the same set in set-associative caches

## Slide 54: More Detailed Mapping Example
1st step: Find data block number that the word belongs to
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  Direct mapped
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks

## Slide 55: More Detailed Mapping Example
2nd step: Map the block number to cache block number
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  Direct mapped
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
% 8 blocks
= cache block no. 3
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks

## Slide 56: More Detailed Mapping Example
1st step: Calculate how many sets exist
8 blocks / 4 entries per set = 2 sets
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  4-way Set-Associative
We load a word from 0x77FF1C68
0 |  |  |  | 1 |  |  | 
cache blocks
set no.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks

## Slide 57: More Detailed Mapping Example
2nd step: Find data block number that the word belongs to
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  4-way Set-Associative
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
0 |  |  |  | 1 |  |  | 
cache blocks
set no.

## Slide 58: More Detailed Mapping Example
3rd step: Map the block number to cache block number
0x77FF1C68 = 0111 0111 1111 1111 0001 1100 0110 1000
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  4-way Set-Associative
We load a word from 0x77FF1C68
Offset within a data word
Each data word’s offset
within a block
(2nd word in a block)
Block no.
% 2 sets
= cache block no. 1
0 |  |  |  | 1 |  |  | 
cache blocks
set no.
pick any available block within set 1

## Slide 59: More Detailed Mapping Example
1st and all step: Find any available cache block and map
We have a cache that has following configuration
  Consists of 8 cache blocks (lines)
  A data word is 4-byte
  A block is 32-byte (8 words per block)
  Fully-Associative
We load a word from 0x77FF1C68
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
cache blocks
pick any available block

## Slide 60: Cache Replacement Policy
When loading a new block (on miss), if the cache is already full, which block should be replaced (in the set)?
  Random: Replace a randomly chosen line
  FIFO: Replace the oldest line
  LRU (Least Recently Used): Replace the least recently used line
  Many others: Round Robin, LIFO, MRU, etc..

## Slide 61: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  |  | 
 | 3 (LRU) |  |  |  |  |  |  |  |  | 
cache miss |  | m |  |  |  |  |  |  |  | 

## Slide 62: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B |  |  |  |  |  |  | 
 | 1 |  | A |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  |  | 
 | 3 (LRU) |  |  |  |  |  |  |  |  | 
cache miss |  | m | m |  |  |  |  |  |  | 

## Slide 63: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C |  |  |  |  |  | 
 | 1 |  | A | B |  |  |  |  |  | 
 | 2 |  |  | A |  |  |  |  |  | 
 | 3 (LRU) |  |  |  |  |  |  |  |  | 
cache miss |  | m | m | m |  |  |  |  |  | 

## Slide 64: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D |  |  |  |  | 
 | 1 |  | A | B | C |  |  |  |  | 
 | 2 |  |  | A | B |  |  |  |  | 
 | 3 (LRU) |  |  |  | A |  |  |  |  | 
cache miss |  | m | m | m | m |  |  |  |  | 

## Slide 65: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C |  |  |  | 
 | 1 |  | A | B | C | D |  |  |  | 
 | 2 |  |  | A | B | B |  |  |  | 
 | 3 (LRU) |  |  |  | A | A |  |  |  | 
cache miss |  | m | m | m | m | h |  |  |  | 

## Slide 66: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D |  |  | 
 | 1 |  | A | B | C | D | C |  |  | 
 | 2 |  |  | A | B | B | B |  |  | 
 | 3 (LRU) |  |  |  | A | A | A |  |  | 
cache miss |  | m | m | m | m | h | h |  |  | 
LRU to be replaced for E

## Slide 67: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D | E |  | 
 | 1 |  | A | B | C | D | C | D |  | 
 | 2 |  |  | A | B | B | B | C |  | 
 | 3 (LRU) |  |  |  | A | A | A | B |  | 
cache miss |  | m | m | m | m | h | h | m |  | 

## Slide 68: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D | E | C | 
 | 1 |  | A | B | C | D | C | D | E | 
 | 2 |  |  | A | B | B | B | C | D | 
 | 3 (LRU) |  |  |  | A | A | A | B | B | 
cache miss |  | m | m | m | m | h | h | m | h | 
LRU to be
replaced for G

## Slide 69: LRU Example
Cache configuration:
  Size: 4 blocks
  Mapping: fully-associative
  Replacement: LRU
Mem access sequence: (each character indicates a block address)
  ABCDCDECG
Accesses |  | A | B | C | D | C | D | E | C | G
priority order (LRU) | 0 (MRU) | A | B | C | D | C | D | E | C | G
 | 1 |  | A | B | C | D | C | D | E | C
 | 2 |  |  | A | B | B | B | C | D | E
 | 3 (LRU) |  |  |  | A | A | A | B | B | D
cache miss |  | m | m | m | m | h | h | m | h | m

## Slide 70: Cache Policies: Cases
Allocation policy: do we allocate a block in cache for the missed data?
Read policies:
  Read Hit: this is what we want. Only one data read from the cache.
  Read Miss: needs to fetch from lower level, but just write to the register once after that
    read-allocate (with replacement policy) vs. no-read-allocate (i.e., cache bypassing)
Write policies (only for the data cache): consistency & performance tradeoffs
  Write Hit: behavior and number of writes depends on write policy
    Write-through vs. write-back vs. write-evict
  Write Miss: needs to first read from lower level, then apply write policies
    Write-allocate (with replacement policy): Write-through vs. Write-back
    No-write-allocate (bypassing): Write-evict

## Slide 71: Write Policy: Write-back
Write-back: inconsistent with lower level
  The value is written only to the cache line.
  The modified (dirty) cache line is written to the lower level only when it is evicted.
    1 dirty bit is needed for each cache line.
  A write-back buffer to update lower level with evicted dirty blocks
    Must write a full block at this point since we do not know which word is modified
  Example: assume cache block containing word address A is initially in the cache
A
A
SW to A
A
B
dirty bit (A) = 1
dirty bit (A) = 0

## Slide 72: Write Policy: Write-back
Write-back: inconsistent with lower level
  The value is written only to the cache line.
  The modified (dirty) cache line is written to the lower level only when it is evicted.
    1 dirty bit is needed for each cache line.
  A write-back buffer to update lower level with evicted dirty blocks
    Must write a full block at this point since we do not know which word is modified
  Example: assume cache block containing word address A is initially in the cache
A
LW B
A
B
A few cycles later...
L1 is full and A is selected to be replaced by B
dirty bit (A) = 1
If A was not modified (dirty bit = 0) when replaced, A is not updated to lower mem.

## Slide 73: Write Policy: Write-through
Write-through: consistent with lower level
  The value is written to both the cache line and the lower-level memory.
    No need to write a full block to the lower level (e.g., only write 4B for a SW)
  Write buffer can be used so cache does not need to wait for the write to lower level
    stall only if the write buffer is full
  Example: assume cache block containing word address A is initially in the cache
A
A
SW to A
A
A

## Slide 74: Write Policy: Write-through
Write-through: consistent with lower level
  The value is written to both the cache line and the lower-level memory.
    No need to write a full block to the lower level (e.g., only write 4B for a SW)
  Write buffer can be used so cache does not need to wait for the write to lower level
    stall only if the write buffer is full
  Example: assume cache block containing word address A is initially in the cache
A
A
A

## Slide 75: Write Policy: Write-evict
Write-evict (no-write): no consistency issue
  The value is written only to the lower level (i.e., bypassing).
  No need to fetch the data first if it is missing in the cache
  If the block containing the write address exists in the cache, evict it.
  The write only needs to send the data specified by the store instruction (e.g., 4 Bytes).
  Write buffer can be used so cache does not need to wait for the write to lower level
  More expensive when there is read after write

## Slide 76: Cache Miss Behavior Analysis
Read miss:
  +Write-through: evict victim block + fetch block from lower level
  +Write-back: evict victim block + write back evicted block if dirty + fetch block from lower level
  +No-write: find victim block + fetch block from lower level
Write miss:
  Write-allocate:
    +Write-through: evict victim block + fetch block from lower level + store word to block + store word to lower level
    +Write-back: evict victim block + write back evicted block if dirty + fetch block from lower level + store word to block
  No-write-allocate: +Write-evict: store word to lower level directly

## Slide 77: Other Cache Policy details
Some caches support multiple policies
  Can achieve different delay/bandwidth tradeoffs or even dynamically change
Write hit and write miss can use different policies
  E.g., write-hit write-evict + write-miss write-allocate-write-back
Different cache levels can also use different policies
  E.g., L1 use write-evict + L2 use write-back
Cache can also be completely bypassed (not the same as write-evict)
  E.g., bypassing L1

## Slide 78: Reduce Miss Rate (1): Code Optimization
Misses occur if sequentially accessed array elements come from different cache blocks
Code optimizations  No hardware change
  Rely on programmers or compilers
Examples:
  Loop interchange: In nested loops, outer loop becomes inner loop and vice versa
  Loop blocking: partition large array into smaller blocks, thus fitting the accessed array elements into cache size

## Slide 79: Loop Interchange
/* Before */
for (j=0; j<5; j++)
for (i=0; i<5; i++)
x[i][j] = 2*x[i][j]
/* After */
for (i=0; i<5; i++)
for (j=0; j<5; j++)
x[i][j] = 2*x[i][j]
Column-major ordering
Row-major ordering
i
j
i
j
each loop iteration accesses different cache line
The same cache line is accessed for a couple of iterations
Assume: cache line size = 5 words
What addresses are accessed in each iteration of inner loop?
five consecutive words belong to a cache line

## Slide 80: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 81
X
=
Loop Blocking
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 82: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 83: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 84: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.
In the traditional matrix multiplication:

## Slide 85: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
The second matrix may always encounter misses because individual data are from different cache blocks
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 86: Loop Blocking
X
=
/* Before */
for (i=0; i<N; i++)
for (j=0; j<N; j++)
for (k=0; k<N; k++)
C[i][j] = C[i][j] + A[i][k] * B[k][j];
If N is large, the cache line that has been accessed is likely to be replaced before next access
In the traditional matrix multiplication:
To generate one output element (red color), the 6 elements of each input matrix (gray color) will be accessed.

## Slide 87: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
Matrix is computed in a smaller block unit
 higher locality
In the block-based matrix multiplication:

## Slide 88: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 89: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 90: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 91: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 92: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 93: Loop Blocking
X
=
/* After (block size = 4) */
for (i=0; i<N; i=i+b)
for (j=0; j<N; j=j+b)
for (k=0; k<N; k=k+b)
for (ii=i; ii<i+b; ii++)
for (jj=j; jj<j+b; jj++)
for (kk=k; kk<k+b; kk++)
C[ii][jj] = C[ii][jj] + A[ii][kk] * B[kk][jj];
In the block-based matrix multiplication:

## Slide 94: Reduce Miss Rate (2): Reduce the 3 C’s
Increase Cache Size
  Reduce miss for: capacity miss, conflict miss
  But has many limitations
Increase Associativity (cache size unchanged)
  Reduce miss for: conflict miss
  But may increase access latency
Increase Cache Block Size (cache size unchanged)
  Reduce miss for: compulsory
  But may increase miss penalty (more data will be evicted and fetched)
  Very large blocks could increase miss rate (i.e., increase capacity miss)
Compulsory (cold) Misses
Capacity Misses
Conflict Misses

## Slide 95: Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Cache size – the larger the better
Block size – tradeoffs
Why?

## Slide 96: Block Size Tradeoff
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks -- increases capacity misses
Block Size
Average
Access
Time
Increased Miss Penalty
& Miss Rate
Block Size
Average Memory Access Time = Hit Time + Miss Penalty x Miss Rate

## Slide 97: Benefits of Set Associative Caches
Data from Hennessy & Patterson, Computer Architecture
Largest gains when going from direct mapped to 2-way (20%+ reduction in miss rate)

## Slide 98: Reduce Miss Rate (3): Policies
Use appropriate policies
  LRU + write-back works for most applications
  Many GPUs use write-hit write-evict + write-miss no-write-allocate
  Can even dynamically change policy according to profiling
Use more advanced policies
  E.g., ML based

## Slide 99: Reduce Miss Rate (4): Multi-level Caches
Having a unified L2 cache (i.e., it holds both instructions and data) and in some cases even a unified L3 cache
L1 cache should focus on minimizing hit time in support of a shorter clock cycle
Secondary cache(s) should focus on reducing miss rate to reduce the penalty of long main memory access times

## Slide 100: Split vs. Unified Caches
Split L1I$ and L1D$: to optimize thit
  Low capacity/associativity/block size (reduce thit)
  Minimize structural hazards
  Can optimize L1I$ for wide output and no writes
Unified L2: to optimize hit rate
  thit is less important due to less frequent accesses & long delay already
  High capacity/associativity/block size (reduce %miss)
    Unused instr capacity can be used for data (fewer capacity misses)
    Instr / data conflicts (small to no increase for conflict misses in a large cache)
  Instr / data structural hazards are rare (would take a simultaneous L1I$ and L1D$ miss)

## Slide 101: Reduce Miss Rate (5): Prefetching
Hardware prefetching
  Fetch blocks into the cache proactively (speculatively)
  Key is to anticipate the upcoming miss addresses accurately
  Relies on having unused memory bandwidth available
A simple case is to use next block prefetching
  Miss on address X → anticipate next reference miss on X + block-size
  Works well for instructions (sequential execution) and for arrays of data
Need to initiate prefetches sufficiently in advance
If prefetched instruction/data is not used, the cache is polluted with unnecessary data (possibly evicting useful data)

## Slide 102: Measuring Performance with Caches
Assuming cache hit costs are included as part of the normal CPU execution cycle, then
  CPU time = IC × CPI × CP
  = IC × (CPIideal + Memory-stall cycles) × CP
CPIstall
Memory-stall cycles come from cache misses (a sum of read-stalls and write-stalls)
  Read-stall cycles = read miss ratio × read miss penalty
  Write-stall cycles = write miss ratio × write miss penalty + write buffer stalls
For write-through caches, we can simplify this to
  Memory-stall cycles = miss ratio × miss penalty
Note: this is miss ratio with regard to all instructions (not only LW)
= read ratio * cache miss rate

## Slide 103: Measuring Performance with Caches
Example: A processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instructions, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  CPIstalls = 2 + 3.44 = 5.44

## Slide 104: Other than Miss Rates
Cache bypassing (e.g., L1D)
  Reduce latency if L1 misses
Sector cache
  Fetch only a portion of the cache line
  Not the same as reducing cache line size
Value prediction
  Using history value to predict future values
  Roll back if predict wrong
  Or accept a certain quality loss if the application is error tolerant

## Slide 105: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Connected to an on-die memory controller

## Slide 106: DRAM Cells
A DRAM cell consists of a capacitor and an access transistor
It stores data in terms of charge in the capacitor
Cheaper and larger than SRAM
  A DRAM chip consists of (10s of 1000s of) rows of such cells
wordline
bitline
bitline
bitline
(row enable)
row
column
column
column

## Slide 107: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Dynamic (i.e., never in a stable state)
  Activate each row every N ms (e.g., typical N = 64)
Downsides of refresh
  Energy consumption: Each refresh consumes energy
  Performance degradation: DRAM rank/bank unavailable while refreshed
  QoS/predictability impact: (Long) pause times during refresh
  Refresh rate limits DRAM capacity scaling

## Slide 108: Recall: SRAM Cache Design
r
o
w
d
e
c
o
d
e
r
row
address
4-bit data word
SRAM Cell
Array
word (row)
select line
bit (data) lines
Each intersection represents a
6-T SRAM cell
Column Selector &
I/O Circuits
column
address
Each row holds a data block
Column address selects the requested word from block

## Slide 109: DRAM Design 1: The Classical
data bit
data bit
r
o
w
d
e
c
o
d
e
r
row
Address
(RAS)
Column Selector &
I/O Circuits
column
Address
(CAS)
data bit
bit (data) lines
Each intersection represents a 1-T DRAM cell
The column address selects the requested bit from the row in each plane
data word
. . .
. . .
DRAM Cell Array
word (row) select line
m planes
DRAM Bank

## Slide 110: DRAM Performance Metrics
DRAM addresses are divided into 2 halves (row and column)
  RAS or Row Access Strobe that triggers the row decoder
  CAS or Column Access Strobe that triggers the column selector
Latency: Time to access one word
  Access Time: time taken when word is read or written
    read access and write access times can be different
  Cycle Time: time between successive (read or write) requests
Bandwidth: How much data can be supplied per unit time
  Width of the data channel * channel usage frequency

## Slide 111: DRAM Design 1: The Classical
DRAM Organization:
  N rows x N column x M-bit (planes)
  Reads or Writes M-bit at a time
  Each M-bit access requires a RAS / CAS cycle
Row Address
CAS
RAS
Col Address
Row Address
Col Address
Access Time
Cycle Time
1st M-bit
2nd M-bit

## Slide 112: DRAM Design 1: The Classical
Row Address
CAS
RAS
Col Address
Col Address
1st M-bit
Col Address
Col Address
2nd M-bit
3rd M-bit
4th M-bit
Cycle Time
Page Mode: A row is kept “open” by keeping the RAS asserted
  Pulse CAS to access other M-bit blocks on that row
  Successive reads or writes within the row are faster since don’t have to precharge and (re)access that row

## Slide 113: DRAM Design 2: Synchronous DRAMs
Like page mode DRAMs, synchronous DRAMs (SDRAMs) can transfer a burst of data from a series of sequential addresses in the same row
For words in the same burst, don’t have to provide the complete (row and column) addresses
  The entire row is loaded into a row buffer (SRAM).
  Specify the starting (row+column) address and the burst length (burst must be in the same row).
  Data words in the burst are then accessed from that SRAM under control of a clock signal.

## Slide 114: Synchronous DRAM (SDRAM) Operation
Row Address
CAS
RAS
Col Address
1st
M-bit
http://en.wikipedia.org/wiki/DDR_SDRAM
2nd
M-bit
3rd
M-bit
clock
After RAS loads a row into the SRAM cache
  Input CAS as the starting “burst” address along with a burst length to read a burst of data from a series of sequential addresses within that row on the clock edge
…

## Slide 115: DDR (Double Data Rate) SDRAMs
Row Address
CAS
RAS
Col Address
1st
M-bit
Row Address
http://en.wikipedia.org/wiki/DDR_SDRAM
2nd
M-bit
3rd
M-bit
4th
M-bit
clock
Transfers burst data on both the rising and falling edge of the clock (so twice fast)
  2n core prefectch

## Slide 116: DDR (Double Data Rate) SDRAMs
DDR1 VS DDR1+:
DDR2 vs. QDR

## Slide 117: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Chip:
  Consists of multiple banks (2-16 in Synchronous DRAM)
    Banks works in parallel to overlap delay
  Banks share command/address/data buses
  The chip itself has a narrow interface (4-16 bits per read)

## Slide 118: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Rank:
  Multiple chips operated together to form a wide interface
  All chips comprising a rank are controlled at the same time
    Respond to a single command
    Share address and command buses, but provide different data
  E.g., Using 8 chips with 8-bit interface to form a 64-bit wide Rank

## Slide 119: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
DIMM (dual inline memory module):
  A DRAM module consists of one or more ranks
  This is what you plug into your motherboard

## Slide 120: DIMM (Dual Inline Memory Module)
Contains DRAM chips each have data widths of x4 or x8
  Can be on both sides
Can have more than one rank
  Increase storage capacity
  Only one rank accessible at a time
SIMM vs DIMM
  DIMM has separate contacts on each side of the board to provides twice as much data rate.

## Slide 121: A 64-bit Wide DIMM (One Rank)
Advantages:
  Acts like a high-capacity DRAM chip with a wide interface
  Flexibility: memory controller does not need to deal with individual chips
Disadvantages:
  Granularity: Accesses cannot be smaller than the interface width

## Slide 122: DRAM Subsystem Organization
  Dram: Dynamic RAM
DRAM Organization:
Channel
DIMM
Rank
Chip
Bank
Row/Column
Channel: Independent memory subsystem
  E.g., 2 independent Channels:

## Slide 123: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”
Each channel is connected to its own on-die memory controller

## Slide 124: Row Operations & Row Buffer Locality
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 1, Column 0)
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address: Row Operation:
R0
R0
R1
Activation
Restore, Precharge, Activation
No operation
RBL=2
RBL=1
Credit: Onur Mutlu.
Improving Row Buffer Locality (RBL) is the key to improve DRAM efficiency

## Slide 125: RBL & Memory Scheduling Schemes
……
Activation Counter:
R1: Activation = 1
R5: Activation = 2
R1: Activation = 3
R5: Activation = 4
R5: Activation = 4
Avg RBL = 5 / 4 = 1.25
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
In-order scheduling
(FIFO):
Request Stream
R5
……
Activation Counter:
R1: Activation = 1
R1: Activation = 1
R5: Activation = 2
R5: Activation = 2
R5: Activation = 2
Avg RBL = 5 / 2 = 2.5
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
Out-of-order scheduling
(FR-FCFS):
Request Stream
R5
Visible to the memory scheduler
Same
activation
Same
activation
Same
activation
Row Buffer Locality

## Slide 126: DRAM Milestones
In the time that the memory to processor bandwidth has more than doubled the memory latency has improved by a factor of only 1.2 to 1.4
 | DRAM | Page DRAM | Page DRAM | Page DRAM | SDRAM | DDR SDRAM
Module Width | 16b | 16b | 32b | 64b | 64b | 64b
Year | 1980 | 1983 | 1986 | 1993 | 1997 | 2000
Mb/chip | 0.06 | 0.25 | 1 | 16 | 64 | 256
Die size (mm2) | 35 | 45 | 70 | 130 | 170 | 204
Pins/chip | 16 | 16 | 18 | 20 | 54 | 66
BWidth (MB/s) | 13 | 40 | 160 | 267 | 640 | 1600
Latency (nsec) | 225 | 170 | 125 | 75 | 62 | 52
Patterson, CACM Vol 47, #10, 2004

## Slide 127: Review: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 128: Magnetic Disk
Purpose: Long term, nonvolatile storage
  Lowest level in the memory hierarchy: large, cheap, slow
General structure
  1 to 4 rotating platter coated with a magnetic surface (2 sides recordable)
    Rotational speeds of 5,400 to 15,000 RPM
  Moveable read/write head to access the information for each platter
  10,000 to 50,000 tracks per surface
    Cylinder - all the tracks under the head at a given point on all surfaces
  100 to 500 sectors per track
    The smallest unit that can be read/written (typically 512B)
    Outer tracks can hold more sectors than the inner tracks
Sector
Track
Cylinder
Head
Platter
Controller
+
Cache

## Slide 129: Magnetic Disk Characteristic
  Rotational latency: wait for the desired sector to rotate under the head
    ½ of 1/RPM converted to ms: 0.5R/5400RPM = 5.6ms to 0.5R/15000RPM = 2.0ms
  Transfer time: transfer a block of bits (one or more sectors) under the head to the disk controller’s cache (70 to 125 MB/s are typical disk transfer rates)
    the disk controller’s “cache” takes advantage of spatial locality in disk accesses
    cache transfer rates are much faster (e.g., 375 MB/s)
  Controller time: the overhead the disk controller imposes in performing a disk I/O access (typically < 0.2 ms)
Sector
Track
Cylinder
Head
Platter
Controller
+
Cache
  Seek time: position the head over the proper track
    3 to 12/15 ms on average
    Due to locality of disk references, the actual average seek time may be only 25% to 33% of the advertised number

## Slide 130: Typical Disk Access Time
  If the measured average seek time is 25% of the advertised average seek time, then
Avg disk read/write
= 4.0 ms + 0.5/(15,000RPM/(60sec/min)) + 0.5KB/(100MB/sec) + 0.2 ms
= 4.0 + 2.0 + 0.005 + 0.2 = 6.2 ms
Avg disk read/write = 1.0 + 2.0 + 0.005 + 0.2 = 3.2 ms
The average time to read or write a 512B sector for a disk rotating at 15,000 RPM with average seek time of 4 ms, a 100MB/sec transfer rate, and a 0.2 ms controller overhead

## Slide 131: Disk Latency & Bandwidth Improvement
Disk latency = average seek time + rotational latency.
Disk bandwidth is the peak transfer speed of formatted data from the media (not from the cache).
Patterson, CACM Vol 47, #10, 2004
Chart: Year of Introduction
| 1983 | 1990 | 1994 | 1998 | 2003
Bandwidth (MB/s) | 0.6 | 4 | 9 | 24 | 86
Latency (msec) | 48.3 | 17.1 | 12.7 | 8.8 | 5.7

## Slide 132: How is the Hierarchy Managed?
registers  memory
  by compiler (or programmer)
registers  cache  main memory
  by the cache & memory controller hardware
main memory  external storage (flash, disk)
  Static: by the programmer with OS support (files)
  Dynamic: by the operating system (virtual memory)
    virtual address to physical address mapping
    assisted by the hardware (TLB, page tables)

## Slide 133: Virtual Memory
Virtual Address (VA)
Page offset
Virtual page number
31 30 . . . 12 11 . . . 0
Page offset
Physical page number
Physical Address (PA)
29 . . . 12 11 0
Translation
A virtual address must first be translated to a physical address to access memory
  Basic unit: page (e.g., 1KB to 64KB)
Virtual memory size can be larger than physical memory size
  Pages can be stored in the secondary storage

## Slide 134: Address Space Isolation
Program 1 page table
Main (physical) memory
Program 2 page table
Allows efficient and safe sharing of main memory among multiple processes
  The starting location of each page is contained in the program’s page table
  Create the illusion that each program has a large consecutive memory space
  Improving memory utilization: code can be loaded anywhere the OS can find space
Virtual address space

## Slide 135: Address Translation Mechanisms
Physical page
base addr
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
Page Table (in main memory)
Offset
Physical page #
Offset
Page table register
virtual address
physical address
Page walk: Search (walk) the page table
Page fault: a DRAM miss for the page
 Page in disk

## Slide 136: Virtual Addressing with a Cache
It takes an extra memory access to translate a VA to a PA
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
This makes memory (cache) accesses very expensive
The hardware solution is to use a Translation Lookaside Buffer (TLB)
  A small cache that keeps track of recently used address mappings to avoid having to do a page table lookup in main memory

## Slide 137: Making Address Translation Fast
Physical page
base address
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
1
1
1
0
1
Tag
Physical page
base address
V
TLB
Page Table (in physical memory)
Page table register

## Slide 138: A TLB in the Memory Hierarchy
A TLB miss – is it a page fault or merely a TLB miss?
  If the page is loaded into main memory, then the TLB miss can be handled by loading the translation information from the page table into the TLB (10’s of cycles )
  If the page is not in main memory, then it’s a true page fault (1,000,000’s)
TLB misses are much more frequent than true page faults
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
¾ t
¼ t

## Slide 139: TLB Event Combinations
TLB | Page Table | Cache | Possible? Under what circumstances?
Hit | Hit | Hit | 
Hit | Hit | Miss | 
Miss | Hit | Hit | 
Miss | Hit | Miss | 
Miss | Miss | Miss | 
Hit | Miss | Miss/ Hit | 
Miss | Miss | Hit | 
Yes – this is what we want!
Yes – although the page table is not
checked after the TLB hits
Yes – TLB missed, but PA is in page table and data is in cache
Yes – TLB missed, but PA is in page table, data not in cache
Yes – page fault
No – TLB translation is not possible if the page is not present in main memory
No – data is not allowed in the cache if the
page is not in memory